## Slide 1: MV-HEVC/SHVC HLS: Clean-up for output layer sets (JCTVC-Q0165, JCT3V-H0053)
JCT-VC 17th Meeting: Valencia, ES, 27 Mar. – 4 Apr. 2014
JCT-3V 8th Meeting: Valencia, ES, 29 Mar. – 4 Apr. 2014
Takeshi Tsukuba*, Tomoyuki Yamamoto*, Tomohiro Ikai*, Sachin Deshpande**
*SHARP Corporation
**Sharp Labs of America, Inc.

## Slide 2: Summary
Proposals:
  Restrictions on output layer set to avoid
    1a) output layer set with no output layers
    1b) duplicated output layer sets with the same output layers.
     for avoiding non-comforming bitstream, easy testing
  Signal num_add_output_layer_sets / default_target_output_layer_set when vps_num_layer_sets_minus1 > 0
     for consistency
  Add a gating flag and inference rule for profile_level_tier_idx/DPB parameters in additional output layer sets  for bit reduction

## Slide 3: Proposal 1
Current draft:
  Output layer can be explicitly defined by output_layer_flag.
Problem :
Non-conforming or confusing output layer sets can exist
  Output layer sets without any output layer
  Duplicated output layer set definition on the same layer set
Solution: add restrictions in output_layer_flag semantics.
When LayerSetIdxForOutputLayerSet[iA] is equal to LayerSetIdxForOutputLayerSet[iB] for any iA and iB in the range of 0 to NumOutputLayerSets-1, inclusive, with iA not equal to iB, at least one of the following conditions shall be true:
- the value of OutputLayerFlag[iA][n] is not equal to OutputLayerFlag[iB][n] for at least one value of n in the range of 0 to NumLayerInIdList[ LayerSetIdxForOutputLayerSet[iA] ] – 1, inclusive.
- the value of AltOuputLayerFlag[iA] is not equal to AltOutputLayerFlag[iB].
- the value of profile_level_tier_idx[iA] is not equal to profile_level_tier_level_idx[iB].
It is requirement of bitstream comformance that the i-th output layer set shall have one or more output layers.
Or
The sum of OutputLayerFlag[ i ][ j ] for j in the range of 0 to NumLayersInIdList[ LayerSetIdxForOutputLayerSet[ i ] ] − 1, inclusive shall be greater than 0.
For a)
For b)

## Slide 4: Proposal 2
Current draft:
  num_add_output_layer_sets is always signaled.
  default_target_output_layer_idc is signaled when NumOutputLayerSets >0.
Problem :
  Allowing additional output layer set when one layer set exits only brings undesirable definition
  Not consistent with default_targtet_ouput_layer_idc signalling
Solution:
  Signal both syntax when vps_num_layer_sets_minus1 is greater than 0.
vps_extension( ) { | Descriptor
… | 
if (vps_num_layer_sets_minus1 > 0) | 
{ | 
num_add_output_layer_sets | ue(v)
if( NumOutputLayerSets > 1 ) | 
default_target_output_layer_idc | u(2)
} | 
NumOutputLayerSets = num_add_output_layer_sets + vps_num_layer_sets_minus1 + 1 | 

## Slide 5: Proposal 3
Current draft:
  Output layer sets associated with the same layer set are always explicitly signalled.
Problem :
  Signaling DPB parameters and profile_level_tier_idx of output layer sets associated with the same layer set is redundant.
  (In typical cases, they have the same DPB size and the same profile/level. )
Solution:
  Add a gating flag, ptl_dpb_info_present_flag, for profile_level_tier_idx/DPB parameters of additional output layer sets
  When not exist, inferred from corresponding non-additional output layer set

## Slide 6: Functionality achieved by Proposal 3
LS#A
Layer Set
OLS#A
OLS#X
OLS#Y
OLS#Z
Output layer set
LayerSetIdx = A
DPB_INFO#A
DPB_INFO#X
DPB_INFO#Y
DPB_INFO#Z
DPB Info.
ptl_dpb_info_present_flag[i]
1
1
0
0
When ptl_dpb_info_present_flag[i] is equal to 0,
DPB info. for i-th additional output layer sets, e.g., DPB_INFO#Y, DPB_INFO#Z, is inferred to be equal to that of the default output layer set(DPB_INFO#A for OLS#A.)
Additional output layer set
Infer
Explicitly signal

## Slide 7: Text changes on Proposal 3
vps_extension( ) { | Descriptor
... | 
for( i = 1; i < NumOutputLayerSets; i++ ) { | 
… | 
if ( i >vps_num_layer_sets_minus1) | 
ptl_dpb_info_present_flag[ i ] | u(1)
if ( ptl_dpb_info_present_flag[ i ] ) | 
profile_level_tier_idx[ i ] | u(v)
… | 
} | 
... | 
dpb_size() | 
... | 
} | 
ptl_dpb_info_present_flag[ i ] equal to 1 specifies that the syntax profile_level_tier_level_idx[ i ] and sub_layer_flag_info_present_flag[ i ], max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ], max_vps_num_reorder_pics[ i ][ j ] max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ] and max_vps_latency_increase_plus1[ i ][ j ] are present for i-th output layer set. ptl_dpb_info_present_flag[ i ] equal to 0 specifies that the syntax profile_level_tier_level_idx[ i ] and sub_layer_flag_info_present_flag[ i ], max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ], max_vps_num_reorder_pics[ i ][ j ] max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ] and max_vps_latency_increase_plus1[ i ][ j ] are not present for i-th output layer set.
profile_level_tier_idx[ i ] specifies the index, into the list of profile_tier_level( ) syntax structures in the VPS, of the profile_tier_level( ) syntax structure that applies to i-th output layer set. The length of the profile_level_tier_idx[ i ] syntax element is Ceil( Log2( vps_num_profile_tier_level_minus1 + 1 ) ) bits. The value of profile_level_tier_idx[ 0 ] is inferred to be equal to 0. The value of profile_level_tier_idx[ i ] shall be in the range of 0 to vps_num_profile_tier_level_minus1, inclusive. For the i-th output layer set, when ptl_dpb_info_present_flag[ i ] is equal to 0, profile_level_tier_idx[ i ] is inferred to be equal to the value of profile_level_tier_idx[ output_layer_set_idx_minus1[ i ] + 1 ].

## Slide 8: Text changes on Proposal 3
dpb_size( ) { | Descriptor
for( i = 1; i < NumOutputLayerSets; i++ ) { | 
if( ptl_dpb_info_present_flag[ i ]){ | 
sub_layer_flag_info_present_flag[ i ] | u(1)
for( j = 0; j <= MaxSubLayersInLayerSetMinus1[ i ]; j++ ) { | 
… | 
} | 
} | 
} | 
} | 
The variable OlsIdx[i] is set to be equal to (output_layer_set_idx_minus1[ i ]+1) for i in the range of 1 to NumOutputLayerSets-1.
sub_layer_flag_info_present_flag[ i ] equal to 1 specifies that sub_layer_dpb_info_present_flag[ i ][ j ] is present for i in the range of 1 to MaxSubLayersInLayerSetMinus1[ i ], inclusive. sub_layer_flag_info_present_flag[ i ] equal to 0 specifies that, for each value of j greater than 0, sub_layer_dpb_info_present_flag[ i ][ j ] is not present and the value is inferred to be equal to 0.
sub_layer_dpb_info_present_flag[ i ][ j ] equal to 1 specifies that max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ] is present for k in the range of 0 to NumSubDpbs[ LayerSetIdxForOutputLayerSet[ i ] ] − 1, inclusive, for the j-th sub-layer, and max_vps_num_reorder_pics[ i ][ j ] and max_vps_latency_increase_plus1[ i ][ j ] are present for the j-th sub-layer.
sub_layer_dpb_info_present_flag[ i ][ j ] equal to 0 specifies that, the values of max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ] are equal to max_vps_dec_pic_buffering_minus1[ i ][ k ][ j − 1 ] for k in the range of 0 to NumSubDpbs[ LayerSetIdxForOutputLayerSet[ i ] ] − 1, inclusive, and that the values max_vps_num_reorder_pics[ i ][ j ] and max_vps_latency_increase_plus1[ i ][ j ] are set equal to max_vps_num_reorder_pics[ i ][ j ‑ 1 ] and max_vps_latency_increase_plus1[ i ][ j ‑ 1 ], respectively. The value of sub_layer_dpb_info_present_flag[ i ][ 0 ] for any possible value of i is inferred to be equal to 1.
When not present, the value of sub_layer_dpb_info_present_flag[ i ][ j ] for j greater than 0 and any possible value of i, is inferred to be equal to 0.

## Slide 9: Text changes on Proposal 3
max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ] plus 1 specifies the maximum required size of the k-th sub-DPB for the CVS in the i-th output layer set in units of picture storage buffers when HighestTid is equal to j.
When j is greater than 0, max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ] shall be greater than or equal to max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ‑ 1 ].
When ptl_dpb_info_present_flag[ i ] is equal to 1 and max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ] is not present for j in the range of 1 to MaxSubLayersInLayerSetMinus1[ i ], inclusive, it is inferred to be equal to max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ‑ 1].
When ptl_dpb_info_present_flag[ i ] is equal to 0 and max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ] is not present for j in the range of 1 to MaxSubLayersInLayerSetMinus1[ i ], inclusive, max_vps_dec_pic_buffering_minus1[ i][ k][ j ] is inferred to be equal to the value of max_vps_dec_pic_buffering_minus1[ OlsIdx[i] ][ k][ j ].
max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ] plus 1 specifies the maximum number of decoded pictures, of the k-th layer for the CVS in the i-th output layer set, that need to be stored in the DPB when HighestTid is equal to j.
When j is greater than 0, max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ] shall be greater than or equal to max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ‑ 1 ].
When ptl_dpb_info_present_flag[ i ] is equal to 1 and max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ] is not present for j in the range of 1 to vps_max_sub_layers_minus1 − 1, inclusive, it is inferred to be equal to max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ‑ 1].
When ptl_dpb_info_present_flag[ i ] is equal to 0 and max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ] is not present for j in the range of 1 to vps_max_sub_layers_minus1 − 1, inclusive, max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ] is inferred to be equal to the value of max_vps_layer_dec_pic_buff_minus1 [ OlsIdx[i] ][ k][ j ].

## Slide 10: Text changes on Proposal 3
max_vps_num_reorder_pics[ i ][ j ] specifies, when HighestTid is equal to j, the maximum allowed number of access units containing a picture with PicOutputFlag equal to 1 that can precede any access unit auA that contains a picture with PicOutputFlag equal to 1 in the i-th output layer set in the CVS in decoding order and follow the access unit auA that contains a picture with PicOutputFlag equal to 1 in output order.
When ptl_dpb_info_present_flag[ i ] is equal to 1 and max_vps_num_reorder_pics[ i ][ j ] is not present for j in the range of 1 to MaxSubLayersInLayerSetMinus1[ i ], inclusive, due to sub_layer_dpb_info_present_flag[ i ][ j ] being equal to 0, it is inferred to be equal to max_vps_num_reorder_pics[ i ][ j ‑ 1].
When ptl_dpb_info_present_flag[ i ] is equal to 0 and max_vps_num_reorder_pics[ i ][ j ] is not present for j in the range of 1 to MaxSubLayersInLayerSetMinus1[ i ], inclusive, max_vps_num_reorder_pics[ i][ j ] is inferred to be equal to the value of max_vps_num_reorder_pics [ OlsIdx[i] ] [ j ].
max_vps_latency_increase_plus1[ i ][ j ] not equal to 0 is used to compute the value of VpsMaxLatencyPictures[ i ][ j ], which, when HighestTid is equal to j, specifies the maximum number of access units containing a picture with PicOutputFlag equal to 1 in the i-th output layer set that can precede any access unit auA that contains a picture with PicOutputFlag equal to 1 in the CVS in output order and follow the access unit auA that contains a picture with PicOutputFlag equal to 1 in decoding order.
When ptl_dpb_info_present_flag[ i ] is equal to 1 and max_vps_latency_increase_plus1[ i ][ j ] is not present for j in the range of 1 to MaxSubLayersInLayerSetMinus1[ i ], inclusive, due to sub_layer_dpb_info_present_flag[ i ][ j ] being equal to 0, it is inferred to be equal to max_vps_latency_increase_plus1[ i ][ j ‑ 1 ].
When ptl_dpb_info_present_flag[ i ] is equal to 0 and max_vps_latency_increase_plus1[ i ][ j ] is not present for j in the range of 1 to MaxSubLayersInLayerSetMinus1[ i ], inclusive, max_vps_latency_increase_plus1 [ i][ j ] is inferred to be equal to the value of max_vps_latency_increase_plus1 [ OlsIdx[i] ] [ j ].

## Slide 11
Thank you!

## Slide 12: Bit amount analysis on proposal 3
Two use-cases are studied.
  Use-case#1: Two output layer sets associated with the same layer set, which have the same output layers and different AltOptLayerFlag values.
  Use-case#2: Three output layer sets associated with the same layer set, which have different output layers and the same AltOptLayerFlag.
Bit-savings are estimated on the condition that profile and DPB info can be inferred and omitted.
Bit-overhead are estimated on the condition that all profile and DPB info are signaled.
 | bit-saving scenario | bit-overhead scenario
Use-case#1 | 49.23 % | -0.77%
Use-case#2 | 66.61% | -0.53 %
Bit-saving ratio compared to ref.(SHVC/MV-HEVC)
100*(ref.- proposal)/ref. [%]

## Slide 13: Use-case#1 (bit-saving scenario)
Use-case#1:
1) There are two output layer sets (OLS#1,OLS#2) associated with the same layer set (LS#1), which have different AltOptLayerFlag (Alt) values. and the same output layers (OptLayer).
LS#1 = { Layer0, Layer1},
OLS#1 = { LS#1, OptLayer={Layer1}, Alt=1},
OLS#2 = { LS#1, OptLayer={Layer1}, Alt=0}
OLS#2 is an additional output layer set against OLS#1.
2) profile_level_tier_idx/DPB size for additional output layer sets are inferred and omitted
( ptl_dpb_info_present_flag is 0 for additional output layer sets)
Assumption:
num. of sub-layers is equal to 4.
DPB sizes of OLS#1 to OLS#2 are the same so that DPB size of OLS#2 are inferred to be equal to OLS#1.
profile_level_tier_idx of OLS#1 to OLS#2 are the same so that profile_level_tier_idx of OLS#2 are inferred to be equal to OLS#1.
NumSubDpbs is equal to NumLayersInIdList[] since all layers's representaion format differ.
Use-case#1 (bit-saving case) |  |  |  |  |  | 
Required bit-size for OLS#1 to OLS#2 |  | Ref. (SHVC/MV-HEVC) |  | Proposal |  | bit-saving
 | bits/OLS | Counts | Total size (bits) | Counts | Total size (bits) | 
Required bit-size on ptl_dpb_info_present_flag | 1 | 0 | 0 | 1 | 1 | N/A
Required bit-size on profile_level_tier_idx | 1 | 2 | 2 | 1 | 1 | 50.00%
Required bit-size on DPB Size syntax element | 64 | 2 | 128 | 1 | 64 | 50.00%
 |  | Total size | 130 |  | 66 | 49.23%

## Slide 14: Use-case#1 (bit-overhead scenario)
Use-case#1:
1) There are two output layer sets (OLS#1,OLS#2) associated with the same layer set (LS#1), which have different AltOptLayerFlag (Alt) values. and the same output layers (OptLayer).
LS#1 = { Layer0, Layer1},
OLS#1 = { LS#1, OptLayer={Layer1}, Alt=1},
OLS#2 = { LS#1, OptLayer={Layer1}, Alt=0}
OLS#2 is an additional output layer set against OLS#1.
2) profile_level_tier_idx/DPB size for additional output layer sets are explicitly signaled
( ptl_dpb_info_present_flag is 1 for additional output layer sets)
Assumption:
num. of sub-layers is equal to 4.
DPB sizes of OLS#1 to OLS#3 are explicitly signaled although DPB sizes of OLS#1 to OLS#2 are the same
profile_level_tier_idx of OLS#1 to OLS#3 are explicitly signaled although profile_level_tier_idx of OLS#1 to OLS#2 are the same.
NumSubDpbs is equal to NumLayersInIdList[] since all layers's representaion format differ.
Use-case#1 (bit-overhead case) |  |  |  |  |  | 
Required bit-size for OLS#1 to OLS#2 |  | Ref. (SHVC/MV-HEVC) |  | Proposal |  | bit-saving
 | bits/OLS | Counts | Total size (bits) | Counts | Total size (bits) | 
Required bit-size on ptl_dpb_info_present_flag | 1 | 0 | 0 | 1 | 1 | N/A
Required bit-size on profile_level_tier_idx | 1 | 2 | 2 | 2 | 2 | 0.00%
Required bit-size on DPB Size syntax element | 64 | 2 | 128 | 2 | 128 | 0.00%
 |  | Total size | 130 |  | 131 | -0.77%

## Slide 15: Use-case#2 (bit-saving scenario)
Use-case#2:
1)There are three output layer sets (OLS#1,2,3) associated with the same layer set (LS#1), which have the same AltOptLayerFlag and different output layers:
- LS#1 = { Layer0, Layer1, Layer2},
- OLS#1 = { LS#1, OptLayer={Layer0, Layer1, Layer2}, Alt=0} ,
- OLS#2 = { LS#1, OptLayer={Layer1,Layer2}, Alt=0} , - OLS#3 = { LS#1, OptLayer={Layer0,Layer1}, Alt=0}
OLS#2 and OLS#3 are additional output layer sets against OLS#1.
2) profile_level_tier_idx/DPB size for additional output layer sets are inferred and omitted
( ptl_dpb_info_present_flag is 0 for additional output layer sets)
Assumption:
num. of sub-layers is equal to 4.
DPB sizes of OLS#1 to OLS#3 are the same so that DPB size of OLS#2 to OLS#3 are inferred to be equal to OLS#1.
profile_level_tier_idx of OLS#1 to OLS#3 are the same so that profile_level_tier_idx of OLS#2 to OLS#3 are inferred to be equal to OLS#1.
NumSubDpb is equal to 1 since all layers' representation formant are the same.
Use-case#2 (bit-saving case) |  |  |  |  |  | 
Required bit-size for OLS#1 to OLS#2 |  | Ref. (SHVC/MV-HEVC) |  | Proposal |  | bit-saving
 | bits/OLS | Counts | Total size (bits) | Counts | Total size (bits) | 
Required bit-size on ptl_dpb_info_present_flag | 1 | 0 | 0 | 2 | 2 | N/A
Required bit-size on profile_level_tier_idx | 1 | 3 | 3 | 1 | 1 | 66.77%
Required bit-size on DPB Size syntax element | 124 | 3 | 372 | 1 | 124 | 66.77%
 |  | Total size | 375 |  | 127 | 66.13%

## Slide 16: Use-case#2 (bit-overhead scenario)
Use-case#2:
1)There are three output layer sets (OLS#1,2,3) associated with the same layer set (LS#1), which have the same AltOptLayerFlag and different output layers:
- LS#1 = { Layer0, Layer1, Layer2},
- OLS#1 = { LS#1, OptLayer={Layer0, Layer1, Layer2}, Alt=0} ,
- OLS#2 = { LS#1, OptLayer={Layer1,Layer2}, Alt=0} , - OLS#3 = { LS#1, OptLayer={Layer0,Layer1}, Alt=0}
OLS#2 and OLS#3 are additional output layer sets against OLS#1.
2) profile_level_tier_idx/DPB size for additional output layer sets are explicitly signaled
( ptl_dpb_info_present_flag is 1 for additional output layer sets)
Assumption:
num. of sub-layers is equal to 4.
DPB sizes of OLS#1 to OLS#3 are the same so that DPB size of OLS#2 to OLS#3 are inferred to be equal to OLS#1.
profile_level_tier_idx of OLS#1 to OLS#3 are the same so that profile_level_tier_idx of OLS#2 to OLS#3 are inferred to be equal to OLS#1.
NumSubDpb is equal to 1 since all layers' representation formant are the same.
Use-case#2 (bit-saving case) |  |  |  |  |  | 
Required bit-size for OLS#1 to OLS#2 |  | Ref. (SHVC/MV-HEVC) |  | Proposal |  | bit-saving
 | bits/OLS | Counts | Total size (bits) | Counts | Total size (bits) | 
Required bit-size on ptl_dpb_info_present_flag | 1 | 0 | 0 | 2 | 2 | N/A
Required bit-size on profile_level_tier_idx | 1 | 3 | 3 | 3 | 3 | 0.00%
Required bit-size on DPB Size syntax element | 124 | 3 | 372 | 3 | 372 | 0.00%
 |  | Total size | 375 |  | 377 | -0.53%