## Slide 1: Constraints on the Range of NBDV(JCT3V-H0107)
Y. Zhang, P. Lu and L. Yu (yul@zju.edu.cn)

## Slide 2: Background
Neighboring Block Disparity Vector (NBDV) is a estimated disparity vector used for IVMP, VSP and ARP. NBDV is also used to generate the DoNBDV when depth_refinement_flag is equal to 1.
NBDV is used to fetch the texture and depth maps of the reference view.

## Slide 3: Problem Statement
When decoding the dependent texture view, both the texture picture and depth picture of the reference view are needed.
Therefore, compared to HEVC and MV-HEVC, there’s additional bandwidth requirement of transmitting depth sample when decoding texture.
In current design, the range of NBDV is as the same as MV, which is -8191.75 to 8192.
However, the range of all the possible accurate DVs among two views is limited and is often much smaller than the image size. Therefore, the current design may request more bandwidth than it really needs for the coded depth map, which will only be accessed by NBDV.

## Slide 4
Proposed Method
To solve the above problem, we propose to limit the range of NBDV.
In last meeting, JCT3V-G0082 proposed to calculate the range of NBDV according to the possible disparity range between the current texture view and the reference view using camera parameters. It was commented that JCT3V-G0082 didn’t improve the worst case thus further study is needed.
In this proposal, the allowable range of NBDV is set to a predefined constant to improve the worst case.
  Horizontal : −1023.75 to 1024 luma samples
  Vertical : [-CtbSizeY+0.25, CtbSizeY] luma samples

## Slide 5
Proposed Method
 | Before Limitation |  |  | After Limitation |  |  | Ratio
Format nickname | Width | Height | Size | Width | Height | Size | 
XGA | 1024 | 768 | 786432 | 1024 | 192 | 196608 | 25.0%
720p HD | 1280 | 720 | 921600 | 1280 | 192 | 245760 | 26.7%
4VGA | 1280 | 960 | 1228800 | 1280 | 192 | 245760 | 20.0%
SXGA | 1280 | 1024 | 1310720 | 1280 | 192 | 245760 | 18.8%
525 16SIF | 1408 | 960 | 1351680 | 1408 | 192 | 270336 | 20.0%
16CIF | 1408 | 1152 | 1622016 | 1408 | 192 | 270336 | 16.7%
4SVGA | 1600 | 1200 | 1920000 | 1600 | 192 | 307200 | 16.0%
1080 HD | 1920 | 1080 | 2073600 | 1920 | 192 | 368640 | 17.8%
2Kx1K | 2048 | 1024 | 2097152 | 2048 | 192 | 393216 | 18.8%
2Kx1080 | 2048 | 1080 | 2211840 | 2048 | 192 | 393216 | 17.8%
4XGA | 2048 | 1536 | 3145728 | 2048 | 192 | 393216 | 12.5%
16VGA | 2560 | 1920 | 4915200 | 2048 | 192 | 393216 | 8.0%

## Slide 6
Proposed Method
 | Before Limitation |  |  | After Limitation |  |  | Ratio
Format nickname | Width | Height | Size | Width | Height | Size | 
3616x1536 (2.35:1) | 3616 | 1536 | 5554176 | 2048 | 192 | 393216 | 7.1%
3672x1536 (2.39:1) | 3680 | 1536 | 5652480 | 2048 | 192 | 393216 | 7.0%
3840x2160 (4*HD) | 3840 | 2160 | 8294400 | 2048 | 192 | 393216 | 4.7%
4Kx2K | 4096 | 2048 | 8388608 | 2048 | 192 | 393216 | 4.7%
4096x2160 | 4096 | 2160 | 8847360 | 2048 | 192 | 393216 | 4.4%
4096x2304 (16:9) | 4096 | 2304 | 9437184 | 2048 | 192 | 393216 | 4.2%
7680x4320 | 7680 | 4320 | 33177600 | 2048 | 192 | 393216 | 1.2%
8192x4096 | 8192 | 4096 | 33554432 | 2048 | 192 | 393216 | 1.2%
8192x4320 | 8192 | 4320 | 35389440 | 2048 | 192 | 393216 | 1.1%

## Slide 7
Proposed Text Change
The change of the text is minor.

## Slide 8
Experimental Results
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.4% | 100.8%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 101.1% | 98.0%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 101.6% | 97.1%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 102.1% | 105.0%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 101.0% | 104.3%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 102.1% | 98.1%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.3% | 101.3%
Shark | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 97.5% | 107.6%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.7% | 98.6%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.4% | 103.3%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.5% | 101.5%

## Slide 9: Conclusion
This contribution proposes to limit NBDV into a predefined range.
Such a limitation can reduce the bandwidth for transmitting depth samples when decoding texture component in worst case.
We recommend adopting the proposed constraints on NBDV.

## Slide 10
Thanks ZTE for crosscheck!
Q & A