## Slide 1
Page <number>
Redundancy removal for DMM1 signalling
Xu Chen, Xiaozhen Zheng, Ce Zhu, Yongbin Lin and Jianhua Zheng
Notes: 26/7/31
<number>

## Slide 2: Summary
Page <number>
  The Problem
  The table index in DMM1 is binarizied as a fixed-length code.
- Current method can not take full use of coding bits needed.
Block size | Index number | Coding bits needed | Redundancy
4×4 | 87 | 7 | 27-87=41
8×8 | 767 | 10 | 210-767=257
16×16 | 1351 | 11 | 211-1351=697
32×32 | 1504 | 11 | 211-1504=544

## Slide 3: Proposed
Page <number>
  Code the differential value(Dv) instead of full table index(Ti)
  1. Set constant value(Cv) depending on blocksize
2. Code the differential between full table index and constant value.
3. Signed bit need to be coded if Dv not greater than Cv.
  Result: Save one coding bit when Dv>Cv.
Block size | 4×4 | 8×8 | 16×16 | 32×32
value | 23 | 255 | 327 | 480
 | Dv>Cv | others
Ti | Cv+Dv | Cv+Dv or Cv-Dv
Block size | Coding bits needed
4×4 | 6~7
8×8 | 9~10
16×16 | 10~11
32×32 | 10~11

## Slide 4: Result
Page <number>
HTM10.0r1 Test condition: CTC
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.1% | 0.1% | 0.06% | 0.02% | -0.01% | 99.2% | 80.1% | 95.4%
Kendo | 0.0% | 0.1% | 0.0% | 0.01% | -0.05% | -0.08% | 98.2% | 101.8% | 97.0%
Newspaper_CC | 0.0% | -0.1% | -0.2% | -0.05% | -0.05% | -0.15% | 98.1% | 79.6% | 94.8%
GT_Fly | 0.0% | -0.1% | -0.2% | -0.03% | -0.03% | 0.01% | 97.9% | 105.9% | 98.9%
Poznan_Hall2 | 0.0% | 0.0% | -0.4% | -0.05% | -0.04% | -0.19% | 98.0% | 96.4% | 91.4%
Poznan_Street | 0.0% | -0.1% | 0.0% | -0.01% | -0.01% | -0.03% | 97.6% | 108.2% | 95.0%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.01% | 0.00% | -0.06% | 97.9% | 102.3% | 104.0%
Shark | 0.0% | 0.0% | 0.0% | -0.01% | -0.03% | -0.05% | 97.6% | 93.9% | 92.9%
1024x768 | 0.0% | 0.1% | 0.0% | 0.00% | -0.03% | -0.08% | 98.5% | 87.2% | 95.7%
1920x1088 | 0.0% | 0.0% | -0.1% | -0.02% | -0.02% | -0.07% | 97.8% | 101.3% | 96.4%
average | 0.0% | 0.0% | -0.1% | -0.01% | -0.02% | -0.07% | 98.1% | 96.0% | 96.2%

## Slide 5: Result
Page <number>
HTM10.0r1 Test condition: AI
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.00% | -0.02% | -0.07% | 100.2% | 102.2% | 102.0%
Kendo | 0.0% | 0.0% | 0.0% | 0.00% | -0.02% | -0.09% | 99.9% | 101.1% | 100.7%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.00% | -0.02% | -0.12% | 99.7% | 96.6% | 95.8%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.05% | 100.1% | 96.5% | 95.9%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.07% | 100.2% | 96.3% | 96.1%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.03% | 100.2% | 97.3% | 96.7%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.03% | 100.0% | 95.7% | 96.1%
Shark | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.05% | 100.2% | 98.7% | 96.8%
1024x768 | 0.0% | 0.0% | 0.0% | 0.00% | -0.02% | -0.09% | 99.9% | 100.0% | 99.5%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.05% | 100.1% | 96.9% | 96.3%
average | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.07% | 100.1% | 98.0% | 97.5%

## Slide 6: Additional result
Page <number>
HTM10.0r1 Test condition: CTC(Code the bins with bypass mode)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.1% | -0.1% | 0.01% | -0.02% | 0.00% | 80.7% | 64.7% | 80.1%
Kendo | 0.0% | 0.1% | -0.1% | -0.01% | -0.06% | -0.05% | 81.4% | 77.3% | 79.8%
Newspaper_CC | 0.0% | -0.1% | -0.1% | -0.03% | -0.06% | -0.10% | 81.0% | 64.6% | 78.1%
GT_Fly | 0.0% | 0.0% | -0.2% | -0.02% | -0.01% | 0.10% | 79.8% | 68.2% | 81.6%
Poznan_Hall2 | 0.0% | 0.0% | -0.5% | -0.08% | -0.09% | -0.28% | 78.7% | 74.0% | 78.3%
Poznan_Street | 0.0% | -0.1% | 0.0% | -0.01% | 0.00% | -0.02% | 79.7% | 77.2% | 82.8%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.02% | 79.5% | 73.5% | 85.6%
Shark | 0.0% | -0.2% | -0.1% | -0.03% | -0.06% | -0.09% | 78.6% | 65.8% | 75.1%
1024x768 | 0.0% | 0.0% | -0.1% | -0.01% | -0.05% | -0.05% | 81.0% | 68.9% | 79.3%
1920x1088 | 0.0% | -0.1% | -0.2% | -0.03% | -0.03% | -0.06% | 79.2% | 71.8% | 80.7%
average | 0.0% | 0.0% | -0.1% | -0.02% | -0.04% | -0.06% | 79.9% | 70.7% | 80.2%

## Slide 7: Additional result
Page <number>
HTM10.0r1 Test condition: AI (Code the bins with bypass mode)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.00% | -0.02% | -0.08% | 100.7% | 103.3% | 103.4%
Kendo | 0.0% | 0.0% | 0.0% | 0.00% | -0.02% | -0.08% | 102.6% | 104.8% | 105.0%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.00% | -0.03% | -0.11% | 101.3% | 96.2% | 95.4%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.05% | 100.8% | 97.0% | 97.4%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.07% | 101.7% | 101.1% | 100.4%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.04% | 101.3% | 99.8% | 98.2%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.04% | 101.0% | 99.7% | 100.8%
Shark | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.05% | 99.3% | 98.8% | 97.9%
1024x768 | 0.0% | 0.0% | 0.0% | 0.00% | -0.02% | -0.09% | 101.5% | 101.5% | 101.2%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.05% | 100.8% | 99.3% | 98.9%
average | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.07% | 101.1% | 100.1% | 99.8%

## Slide 8: Conclusions
Page <number>
Redundancy removed and 0.07 coding gain on CTC and AI.
Don't change DMM1 pattern generation mechanism and DMM1 index entropy coding.
Suggest to be adopted.
Thanks for cross-check by LGE

## Slide 9
Page <number>
Thank you!
www.hisilicon.com