## Slide 1
CE3 related: Alignment of WD and HTM for syntax element depth_dc_flag (JCT3V-H0113)
March 2014
LG Electronics
Junghak Nam (junghak.nam@lge.com)

## Slide 2: Summary
Alignment of WD and HTM for syntax element depth_dc_flag
Proposed method
  Solution 1. HTM is aligned to WD
  Solution 2. WD is aligned to HTM
Experimental results
  Solution 1. minor coding loss on synthesized views in AI
Crosscheck
  JCT3V-H0155 (by Samsung)

## Slide 3: Proposed method
In the current 3D-HEVC, syntax element depth_dc_flag is a mismatch in terms of context model between HTM software and WD
  One context is used in WD
  Two contexts are used in HTM
Proposed method
  Solution 1
    HTM is aligned to WD
    The only one context is used in both HTM and WD
    No WD change
  Solution 2
    WD is aligned to HTM
    The two contexts are used in both HTM and WD
    No HTM change (No experiments)
Initialization variable | ctxIdx of depth_dc_flag |  | 
 | 0 | 1 | 2
initValue | 0 | 0 | 64
Initialization variable | ctxIdx of depth_dc_flag |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5
initValue | 0 | 154 | 0 | 154 | 64 | 154

## Slide 4: Experimental results
Experimental results of Solution 1) under CTC
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.05% | -0.10% | 0.00% | -0.02% | 0.02% | 100.1% | 101.6% | 100.2%
Kendo | 0.00% | 0.09% | 0.09% | 0.02% | 0.03% | 0.00% | 100.0% | 99.0% | 98.5%
Newspaper_CC | 0.00% | -0.06% | -0.11% | -0.03% | -0.01% | 0.08% | 99.9% | 106.3% | 98.1%
GT_Fly | 0.00% | 0.00% | -0.07% | -0.01% | 0.00% | 0.04% | 99.5% | 100.6% | 94.4%
Poznan_Hall2 | 0.00% | -0.04% | -0.36% | -0.04% | -0.03% | -0.15% | 99.3% | 101.2% | 98.4%
Poznan_Street | 0.00% | -0.02% | 0.07% | -0.01% | -0.01% | 0.03% | 99.6% | 95.5% | 98.9%
Undo_Dancer | 0.00% | 0.04% | -0.09% | 0.00% | 0.02% | 0.02% | 99.6% | 98.0% | 97.8%
Shark | 0.00% | -0.04% | -0.04% | -0.01% | -0.01% | 0.00% | 99.4% | 97.8% | 101.6%
1024x768 | 0.00% | 0.03% | -0.04% | 0.00% | 0.00% | 0.03% | 100.0% | 102.3% | 99.0%
1920x1088 | 0.00% | -0.01% | -0.10% | -0.01% | -0.01% | -0.01% | 99.5% | 98.6% | 98.2%
average | 0.00% | 0.00% | -0.08% | -0.01% | 0.00% | 0.01% | 99.7% | 100.0% | 98.5%

## Slide 5: Experimental results
Experimental results of Solution 1) under AI
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.00% | 0.00% | 0.00% | 0.02% | 0.08% | 99.2% | 94.3% | 102.5%
Kendo | 0.00% | 0.00% | 0.00% | 0.00% | 0.02% | 0.08% | 99.6% | 101.6% | 101.6%
Newspaper_CC | 0.00% | 0.00% | 0.00% | 0.00% | 0.02% | 0.09% | 99.2% | 109.1% | 105.6%
GT_Fly | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 0.07% | 97.8% | 102.1% | 103.5%
Poznan_Hall2 | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 0.10% | 99.4% | 104.0% | 105.9%
Poznan_Street | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 0.05% | 99.0% | 99.5% | 88.6%
Undo_Dancer | 0.00% | 0.00% | 0.00% | 0.00% | 0.02% | 0.08% | 99.0% | 99.6% | 103.5%
Shark | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 0.08% | 98.2% | 105.0% | 98.5%
1024x768 | 0.00% | 0.00% | 0.00% | 0.00% | 0.02% | 0.08% | 99.3% | 101.7% | 103.2%
1920x1088 | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 0.08% | 98.7% | 102.1% | 100.0%
average | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 0.08% | 98.9% | 101.9% | 101.2%