## Slide 1
Removal of delta DC values for DMM4 (JCT3V-H0116)
March 2014
LG Electronics
Junghak Nam (junghak.nam@lge.com)

## Slide 2: Summary
Proposed method
  Removal of delta DC values for DMM4
Experimental results
  No coding loss on synthesized views
Crosscheck
  JCT3V-H0156 (by Samsung)

## Slide 3
Derivation of Residual idx

## Slide 4: Proposed method
Propose to remove delta DC mode for DMM4
Illustrative Statistics
Ratio of modes when depth_dc_flag is equal to 1
(HTM-10.0 AI configuration)
 | SDC (including HEVC intra & DIM) | DMM1 | DMM4
Balloons | 87.6 | 11.3 | 1.1
Kendo | 89.6 | 9.5 | 0.9
Newspaper | 82.7 | 15.8 | 1.5
GT_Fly | 88.7 | 10.2 | 1.1
Poznan_Hall2 | 87.9 | 11.2 | 0.8
Poznan_Street | 93.3 | 6.3 | 0.5
Shark | 81.0 | 16.8 | 2.2
Undo_Dancer | 90.7 | 8.4 | 0.9

## Slide 5: Proposed WD change

## Slide 6: Experimental results
Removal of delta DC values for DMM4 under CTC
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 100.0% | 100.1% | 103.7%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.1% | 98.1% | 102.6%
Newspaper_CC | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 100.0% | 101.8% | 101.6%
GT_Fly | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.1% | 99.6% | 97.8% | 101.3%
Poznan_Hall2 | 0.0% | 0.0% | -0.1% | -0.1% | -0.1% | -0.1% | 99.1% | 96.6% | 99.0%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.7% | 97.7% | 99.6%
Undo_Dancer | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.1% | 99.3% | 98.7% | 99.7%
Shark | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 99.3% | 100.6% | 99.6%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.1% | 100.0% | 102.6%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.2% | 98.3% | 99.9%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.5% | 98.9% | 100.9%

## Slide 7: Experimental results
Removal of delta DC values for DMM4 under AI
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.5% | 101.7% | 99.3%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.8% | 99.6% | 97.9%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.1% | 99.1% | 98.3%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.4% | 99.7% | 98.6%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.0% | 100.2% | 98.5%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.3% | 99.4% | 98.9%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.2% | 98.9% | 99.2%
Shark | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.4% | 100.1% | 99.4%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.4% | 100.1% | 98.5%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.5% | 99.7% | 98.9%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.4% | 99.8% | 98.8%

## Slide 8: Appendix. cu_extension()