## Slide 1
Advanced Boundary Chain(ABC)
coding for depth intra coding
(JCT3V-H0121)
Mar. 2014
Notes: <number>

## Slide 2: Introduction
This contribution is follow up of JCT3V-G0094
Advanced Boundary Chain (ABC) coding
  Well described even a curved depth pattern
  Removed the inter-component correlation between texture and depth
  Additional segmentation case (from right to bottom side)
The proposed methods show about 0.3% coding gain.
  In synthesized views, ABC coding provides 0.28% and 0.3% coding gains under CTC and AI configurations, respectively.
<number>

## Slide 3: Proposed method
Rearrange chain code
Context model is applied to syntax elements
Additional segmentation case
  The conventional method covers cases start from above or left sides.
  The proposed method can cover the case of segmentation from right side
<number>
Examples of the cases of segmentation by ABC
Start from above side
Start from left side
Start from right side

## Slide 4: Experimental results
Test1: HTM-10.0r1 vs. ABC coding
<number>
<HTM-10.0r1 vs. ABC coding under CTC>
<HTM-10.0r1 vs. ABC coding under AI>
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.15% | 100.9% | 101.3% | 98.1%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.19% | 101.4% | 102.9% | 100.9%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.28% | 101.0% | 99.9% | 102.1%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | -0.27% | 100.2% | 103.5% | 107.1%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.16% | 100.7% | 99.0% | 99.1%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.09% | 100.6% | 101.7% | 107.4%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.45% | 100.6% | 102.8% | 108.7%
Shark | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | -0.43% | 101.8% | 102.7% | 102.1%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.21% | 101.1% | 101.3% | 100.4%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.28% | 100.8% | 101.9% | 104.9%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.25% | 100.9% | 101.7% | 103.2%
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.2% | 0.0% | 0.0% | 0.1% | -0.16% | 99.6% | 103.8% | 101.9%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | -0.20% | 99.1% | 103.4% | 103.3%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | -0.28% | 99.5% | 104.6% | 102.6%
GT_Fly | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | -0.16% | 99.9% | 104.4% | 106.2%
Poznan_Hall2 | 0.0% | 0.1% | -0.5% | -0.1% | 0.1% | -0.43% | 99.5% | 103.0% | 101.6%
Poznan_Street | 0.0% | -0.1% | -0.1% | 0.0% | 0.1% | -0.10% | 99.6% | 104.5% | 105.4%
Undo_Dancer | 0.0% | -0.4% | -0.3% | -0.1% | 0.0% | -0.58% | 99.9% | 103.5% | 103.5%
Shark | 0.0% | -0.3% | -0.1% | 0.0% | 0.2% | -0.21% | 100.0% | 104.1% | 104.1%
1024x768 | 0.0% | 0.1% | 0.0% | 0.0% | 0.2% | -0.21% | 99.4% | 103.9% | 102.6%
1920x1088 | 0.0% | -0.1% | -0.2% | 0.0% | 0.1% | -0.30% | 99.8% | 103.9% | 104.2%
average | 0.0% | -0.1% | -0.2% | 0.0% | 0.1% | -0.27% | 99.6% | 103.9% | 103.6%

## Slide 5: Experimental results
Test2: HTM-10.0r1 vs. ABC with RB segmentation
<number>
<HTM-10.0r1 vs. ABC with RB segmentation under CTC>
<HTM-10.0r1 vs. ABC with RB segmentation under AI>
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.19% | 100.9% | 103.4% | 101.5%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.23% | 101.5% | 101.9% | 100.7%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.36% | 101.0% | 101.0% | 102.6%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | -0.30% | 99.7% | 102.0% | 106.9%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.17% | 100.3% | 102.3% | 106.4%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.11% | 100.0% | 102.3% | 104.0%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.47% | 100.1% | 103.1% | 107.1%
Shark | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | -0.55% | 101.4% | 101.7% | 105.9%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.26% | 101.1% | 102.1% | 101.6%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.32% | 100.3% | 102.3% | 106.1%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.30% | 100.6% | 102.2% | 104.4%
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.1% | -0.1% | 0.0% | 0.1% | -0.18% | 99.7% | 95.0% | 101.2%
Kendo | 0.0% | -0.1% | 0.0% | 0.0% | 0.2% | -0.24% | 99.8% | 100.9% | 100.5%
Newspaper_CC | 0.0% | 0.1% | 0.0% | 0.0% | 0.2% | -0.36% | 99.8% | 99.3% | 97.6%
GT_Fly | 0.0% | -0.1% | -0.2% | 0.0% | 0.1% | -0.10% | 100.2% | 95.9% | 104.7%
Poznan_Hall2 | 0.0% | -0.1% | -0.3% | -0.1% | 0.1% | -0.36% | 99.9% | 105.4% | 101.1%
Poznan_Street | 0.0% | -0.1% | -0.1% | 0.0% | 0.1% | -0.11% | 99.9% | 93.6% | 103.9%
Undo_Dancer | 0.0% | -0.2% | -0.4% | -0.1% | 0.0% | -0.64% | 100.1% | 100.4% | 102.7%
Shark | 0.0% | -0.3% | -0.2% | 0.0% | 0.2% | -0.28% | 100.1% | 96.6% | 96.8%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | -0.26% | 99.8% | 98.4% | 99.7%
1920x1088 | 0.0% | -0.2% | -0.2% | 0.0% | 0.1% | -0.30% | 100.0% | 98.4% | 101.9%
average | 0.0% | -0.1% | -0.2% | 0.0% | 0.1% | -0.28% | 99.9% | 98.4% | 101.1%

## Slide 6: Conclusion
This contribution proposed an Advanced Boundary Chain coding method.
The proposal achieved 0.3% BD-rate gain in synthesized views compared to HTM-10.0r1.
Recommend that the proposed method be adopted into 3D-HEVC
<number>