## Slide 1: JCT3V-H0136: Constraints for depth modeling modes
Hongbin Liu, Ying Chen (Qualcomm)

## Slide 2: Summary
Proposes to constrain split depth of the associated transform tree of DMM (depth modeling mode) coded PU to be zero
  Coding performance
  Has no impact on coding performance

## Slide 3: Introduction
Depth modeling mode: split a PU into two partitions
P1
P0
DMM1
P0
P1
P1
DMM4

## Slide 4: Introduction
Problem
  When split depth of the associated transform tree of DMM coded PU is larger than 0, the PU contains multiple partitions
  In case delta DC is used, only two delta DC are coded for the PU but there are multiple partitions
  In case transform units are of different block sizes, wedgelet index signaled in DMM1 coded PU maybe invalid for some transform unit

## Slide 5: Proposed method
Constrain split depth of the associated transform tree of DMM coded PU to be zero

## Slide 6
Thank you!