## Slide 1: JCT3V-I0069: AHG7: Complexity Assessment on Depth Intra Modes with Simplified Data Flows
Chun-Fu Chen, Chun-Hsi Huang, Gwo Giun Lee National Cheng Kung University

## Slide 2: Abstract
Differences from JCT3V-H0127
  Simplified data flows of segmental depth intra coding is demonstrated.
  Complexity of de-quantization and inverse transform is provided to comprehensively present the complexity when SDC is disabled.
  More coding configurations are considered, e.g., DLT, SDC, and DMM.
Coding performance (DLT, SDC, and DMM are disabled.)
  AI: 1.8% and 10.3% BD-rate increase for video PSNR vs. total bitrate and synth PSNR vs. total bitrate on average
  CTC: 0.7% and 3.6% BD-rate increase for video PSNR vs. total bitrate and synth PSNR vs. total bitrate on average
Fix the spec text with appropriate expressions.

## Slide 3: Outline
Abstract
Simplified data flows of segmental depth intra coding
Complexity assessment – number of operations
Experimental results
Conclusion

## Slide 4: Simplified data flows
DMM 1 and DMM 4: segmental depth intra coding
Pixel-wise process
Segment-wise process
dcPred[0] = dcVal[0] dcPred[1] = dcVal[1]
If (DltFlag == 1)
For 0<= x, y < N: dltIdxPred = DepthValue2Idx[dcPred[wedgePattern[x][y]]] dltIdxResi = DcOffset[xTb][yTb][wedgePattern[x][y]] Recblock[x][y] = Idx2DepthValue[dltIdxPred + dltIdxResi]
Otherwise (DltFlag == 0)
For 0<= x, y < N: Recblock[x][y] = predSamples[x][y] + DcOffset[xTb][yTb][wedgePattern[x][y]]
If (DltFlag == 1)
RecPixel[0] = Idx2DepthValue[DepthValue2Idx[dcPred[0]] + DcOffset[xTb][yTb][0]] RecPixel[1] = Idx2DepthValue[DepthValue2Idx[dcPred[1]] + DcOffset[xTb][yTb][1]]
Otherwise (DltFlag == 0)
RecPixel[0] = dcPred[0] + DcOffset[xTb][yTb][0] RecPixel[1] = dcPred[1] + DcOffset[xTb][yTb][0]
For 0<= x, y < N: Recblock[x][y] = RecPixel[wedgePattern[x][y]]

## Slide 5: Simplified data flows
Pixel-wise process
Angular: segmental depth intra coding
Pixel-wise process
Segment-wise process
Segment-wise process
If (DltFlag == 1)
dcPred[0] = ( predSamples[0][0] + predSamples[0][N − 1] + predSamples[N − 1][ 0 ] + predSamples[N − 1][N − 1] + 2 ) >> 2
For 0<= x, y < N: dltIdxPred = DepthValue2Idx[dcPred[0]] dltIdxResi = DcOffset[xTb][yTb][0] Recblock[x][y] = predSamples[x][y] + Idx2DepthValue[dltIdxPred + dltIdxResi] − dcPred[0]
dltIdxPred = DepthValue2Idx[dcPred[0]] dltIdxResi = DcOffset[xTb][yTb][0] Resi = Idx2DepthValue[dltIdxPred + dltIdxResi] − dcPred[0]
Otherwise (DltFlag == 0)
For 0<= x, y < N: Recblock[x][y] = predSamples[x][y] + DcOffset[xTb][yTb][0]
Resi = DcOffset[xTb][yTb][0]
For 0<= x, y < N: Recblock[x][y] = predSamples[x][y] + Resi

## Slide 6: Number of operations – DMM 1
 | Original, based on spec |  |  |  | Simplified, segment-wise processing |  |  | 
Processes | Comp (1-bit) | Comp. (pixel) | Add/Sub | LUT access | Comp. (1-bit) | Comp. (pixel) | Add/Sub | LUT access
Derive and assign depth partition value | N2+8 | 1 | 5 | 4 | 8 | 1 | 5 | 4
Segmental depth intra coding | 2N2+1 | 0 | N2 | 2N2 | N2+5 | 0 | 2 | 4
Total | 3N2+9 | 1 | N2+5 | 2N2+4 | N2+13 | 1 | 7 | 8
SDC and DLT are enabled (PU is NN)
SDC is enabled but DLT is disabled (PU is NN)
 | Original, based on spec |  |  |  | Simplified, segment-wise processing |  |  | 
Processes | Comp (1-bit) | Comp. (pixel) | Add/Sub | LUT access | Comp. (1-bit) | Comp. (pixel) | Add/Sub | LUT access
Derive and assign depth partition value | N2+8 | 1 | 5 | 0 | 8 | 1 | 5 | 0
Segmental depth intra coding | 2N2+1 | 0 | N2 | 0 | N2+5 | 0 | 2 | 0
Total | 3N2+9 | 1 | N2+5 | 0 | N2+13 | 1 | 7 | 0
Lookup a datum for the storage has just two data is considered as 1-bit comparison.

## Slide 7: Number of operations – DMM 4
 | Original, based on spec |  |  |  | Simplified, segment-wise processing |  |  | 
Processes | Comp (1-bit) | Comp. (pixel) | Add/Sub | LUT access | Comp. (1-bit) | Comp. (pixel) | Add/Sub | LUT access
Contour pattern generation | 0 | N2 | N2 | 0 | 0 | N2 | N2 | 0
Derive and assign depth partition value | N2+8 | 1 | 5 | 4 | 8 | 1 | 5 | 4
Segmental depth intra coding | 2N2+1 | 0 | N2 | 2N2 | N2+5 | 0 | 2 | 4
Total | 3N2+9 | N2+1 | 2N2+5 | 2N2+4 | N2+13 | N2+1 | N2+7 | 8
SDC and DLT are enabled (PU is NN)
SDC is enabled but DLT is disabled (PU is NN)
 | Original, based on spec |  |  |  | Simplified, segment-wise processing |  |  | 
Processes | Comp (1-bit) | Comp. (pixel) | Add/Sub | LUT access | Comp. (1-bit) | Comp. (pixel) | Add/Sub | LUT access
Contour pattern generation | 0 | N2 | N2 | 0 | 0 | N2 | N2 | 0
Derive and assign depth partition value | N2+8 | 1 | 5 | 4 | 8 | 1 | 5 | 4
Segmental depth intra coding | 2N2+1 | 0 | N2 | 2N2 | N2+5 | 0 | 2 | 4
Total | 3N2+9 | N2+1 | 2N2+5 | 2N2+4 | N2+13 | N2+1 | N2+7 | 8
Lookup a datum for the storage has just two data is considered as 1-bit comparison.

## Slide 8: Number of operations – Angular
 | Original, based on spec |  |  |  | Simplified, segment-wise processing |  |  | 
Processes | Comp. (1-bit) | Mul. | Add/Sub | LUT access | Comp. (1-bit) | Mul. | Add/Sub | LUT access
Angular intra prediction | 0 | 4N2 | 4N2+2N | 0 | 0 | 4N2 | 4N2+2N | 0
Segmental depth intra coding | 2N2+1 | 0 | 3N2+3 | 2N2 | 2 | 0 | N2+5 | 2
Total | 2N2+1 | 4N2 | 7N2+2N+3 | 2N2 | 2 | 4N2 | 5N2+2N+5 | 2
SDC and DLT are enabled (PU is NN)
SDC is enabled but DLT is disabled (PU is NN)
 | Original, based on spec |  |  |  | Simplified, segment-wise processing |  |  | 
Processes | Comp. (1-bit) | Mul. | Add/Sub | LUT access | Comp. (1-bit) | Mul. | Add/Sub | LUT access
Angular intra prediction | 0 | 4N2 | 4N2+2N | 0 | 0 | 4N2 | 4N2+2N | 0
Segmental depth intra coding | 2N2+1 | 0 | 3N2+3 | 2N2 | 2 | 0 | N2+5 | 2
Total | 2N2+1 | 4N2 | 7N2+2N+3 | 2N2 | 2 | 4N2 | 5N2+2N+5 | 2
Lookup a datum for the storage has just two data is considered as 1-bit comparison.

## Slide 9: Number of operations for 6464 CU – DMM 1
TU size is equal to PU size, for 6464 PU, 4 3232 TU are applied.
 | SDC OFF + DLT OFF |  |  |  | SDC ON + DLT OFF |  |  | 
PU size | Mul. | Div. | Add/Sub /Comp | LUT access | Mul. | Div. | Add/Sub /Comp | LUT access
64×64 | N/A | N/A | N/A | N/A | 0 | 0 | 4,180 | 16
32×32 | 96,256 | 4,096 | 103,480 | 8,192 | 0 | 0 | 4,180 | 16
16×16 | 53,248 | 4,096 | 59,616 | 8,192 | 0 | 0 | 4,432 | 64
8×8 | 32,768 | 4,096 | 37,760 | 8,192 | 0 | 0 | 5,440 | 256
4×4 | 26,624 | 4,096 | 34,304 | 8,192 | 0 | 0 | 9,472 | 1,024
 | SDC OFF + DLT ON |  |  |  | SDC ON + DLT ON |  |  | 
PU size | Mul. | Div. | Add/Sub /Comp | LUT access | Mul. | Div. | Add/Sub /Comp | LUT access
64×64 | N/A | N/A | N/A | N/A | 0 | 0 | 4,180 | 32
32×32 | 96,256 | 4,096 | 103,480 | 8,208 | 0 | 0 | 4,180 | 32
16×16 | 53,248 | 4,096 | 59,616 | 8,256 | 0 | 0 | 4,432 | 128
8×8 | 32,768 | 4,096 | 37,760 | 8,448 | 0 | 0 | 5,440 | 512
4×4 | 26,624 | 4,096 | 34,304 | 9,216 | 0 | 0 | 9,472 | 2,048
De-quantization and inverse transform are applied when SDC is disabled.

## Slide 10: Number of operations for 6464 CU – DMM 4
TU size is equal to PU size, for 6464 PU, 4 3232 TU are applied.
 | SDC OFF + DLT OFF |  |  |  | SDC ON + DLT OFF |  |  | 
PU size | Mul. | Div. | Add/Sub /Comp | LUT access | Mul. | Div. | Add/Sub /Comp | LUT access
64×64 | N/A | N/A | N/A | N/A | 0 | 0 | 12,372 | 16
32×32 | 96,256 | 4,096 | 111,672 | 8,192 | 0 | 0 | 12,372 | 16
16×16 | 53,248 | 4,096 | 67,808 | 8,192 | 0 | 0 | 12,624 | 64
8×8 | 32,768 | 4,096 | 45,952 | 8,192 | 0 | 0 | 13,632 | 256
4×4 | 26,624 | 4,096 | 42,496 | 8,192 | 0 | 0 | 17,664 | 1,024
 | SDC OFF + DLT ON |  |  |  | SDC ON + DLT ON |  |  | 
PU size | Mul. | Div. | Add/Sub /Comp | LUT access | Mul. | Div. | Add/Sub /Comp | LUT access
64×64 | N/A | N/A | N/A | N/A | 0 | 0 | 12,372 | 32
32×32 | 96,256 | 4,096 | 111,672 | 8,208 | 0 | 0 | 12,372 | 32
16×16 | 53,248 | 4,096 | 67,808 | 8,256 | 0 | 0 | 12,624 | 128
8×8 | 32,768 | 4,096 | 45,952 | 8,448 | 0 | 0 | 13,632 | 512
4×4 | 26,624 | 4,096 | 42,496 | 9,216 | 0 | 0 | 17,664 | 2,048
De-quantization and inverse transform are applied when SDC is disabled.

## Slide 11: Number of operations for 6464 CU – Angular
TU size is equal to PU size, for 6464 PU, 4 3232 TU are applied.
 | SDC OFF + DLT OFF |  |  |  | SDC ON + DLT OFF |  |  | 
PU size | Mul. | Div. | Add/Sub /Comp | LUT access | Mul. | Div. | Add/Sub /Comp | LUT access
64×64 | 112,640 | 4,096 | 120,064 | 8,192 | 16,384 | 0 | 21,000 | 0
32×32 | 112,640 | 4,096 | 120,320 | 8,192 | 16,384 | 0 | 21,000 | 0
16×16 | 69,632 | 4,096 | 76,800 | 8,192 | 16,384 | 0 | 21,536 | 0
8×8 | 49,152 | 4,096 | 55,296 | 8,192 | 16,384 | 0 | 22,656 | 0
4×4 | 43,008 | 4,096 | 51,200 | 8,192 | 16,384 | 0 | 25,088 | 0
 | SDC OFF + DLT ON |  |  |  | SDC ON + DLT ON |  |  | 
PU size | Mul. | Div. | Add/Sub /Comp | LUT access | Mul. | Div. | Add/Sub /Comp | LUT access
64×64 | N/A |  |  |  | 16,384 | 0 | 21,020 | 8
32×32 |  |  |  |  | 16,384 | 0 | 21,020 | 8
16×16 |  |  |  |  | 16,384 | 0 | 21,616 | 32
8×8 |  |  |  |  | 16,384 | 0 | 22,976 | 128
4×4 |  |  |  |  | 16,384 | 0 | 26,368 | 512
De-quantization and inverse transform are applied when SDC is disabled.

## Slide 12: Experimental results
AI configuration: anchor is HTM 11.0; test turns DMM, SDC, and DLT OFF.
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 2.5% | 7.5% | 39.6% | 107.3% | 100.7%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 3.9% | 9.1% | 39.0% | 107.5% | 101.3%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 1.4% | 12.7% | 39.8% | 107.5% | 100.5%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 1.8% | 10.5% | 39.9% | 108.1% | 98.6%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.7% | 11.3% | 39.3% | 101.2% | 99.9%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 4.6% | 40.7% | 118.3% | 104.9%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.5% | 12.4% | 39.9% | 105.4% | 101.6%
Shark | 0.0% | 0.0% | 0.0% | 0.0% | 3.5% | 14.3% | 43.4% | 105.0% | 99.8%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 2.6% | 9.8% | 39.4% | 107.4% | 100.9%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 1.3% | 10.6% | 40.6% | 107.6% | 101.0%
average | 0.0% | 0.0% | 0.0% | 0.0% | 1.8% | 10.3% | 40.2% | 107.5% | 100.9%

## Slide 13: Experimental results
CTC configuration: anchor is HTM 11.0; test turns DMM, SDC, and DLT OFF.
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.1% | 0.1% | 0.0% | 0.6% | 2.3% | 92.8% | 107.8% | 109.2%
Kendo | 0.0% | -0.2% | 0.0% | 0.0% | 1.5% | 3.1% | 93.1% | 99.0% | 100.6%
Newspaper_CC | 0.0% | 0.1% | 0.1% | 0.0% | 0.8% | 6.3% | 91.0% | 95.9% | 98.2%
GT_Fly | 0.0% | 0.3% | 0.3% | 0.1% | 0.4% | 2.1% | 88.8% | 100.4% | 99.8%
Poznan_Hall2 | 0.0% | 0.0% | -0.4% | -0.1% | 0.0% | 2.9% | 89.7% | 101.0% | 100.1%
Poznan_Street | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 2.1% | 89.5% | 99.9% | 99.8%
Undo_Dancer | 0.0% | 1.3% | 1.2% | 0.3% | 0.8% | 5.0% | 91.6% | 100.0% | 100.0%
Shark | 0.0% | 1.0% | 1.3% | 0.2% | 1.2% | 5.4% | 91.1% | 100.4% | 100.3%
1024x768 | 0.0% | -0.1% | 0.1% | 0.0% | 1.0% | 3.9% | 92.3% | 100.9% | 102.7%
1920x1088 | 0.0% | 0.5% | 0.5% | 0.1% | 0.5% | 3.5% | 90.1% | 100.3% | 100.0%
average | 0.0% | 0.3% | 0.3% | 0.1% | 0.7% | 3.6% | 90.9% | 100.6% | 101.0%

## Slide 14: Conclusion
Simplified data flows could present another perspective of complexity.
SDC not only reduces the number of operations but also increases algorithmic performance due to the fact that it codes depth data according to its characteristics.
Coding tools of depth intra modes in 3D-HEVC can provide significant coding gain.
It is recommended to keep monitoring depth intra coding tools in 3D-HEVC while developing. This proposal suggests anchor complexity and benefits brings from these tools.

## Slide 15: Appendix

## Slide 16: Number of operations - De-quantization and inverse transform
Inverse quantization: N2 comparison (1-bit), 2N2 LUT access, 2N2 multiplications, N2 divisions
  For 0 <= x, y < N m = (scaling_list_enabled_flag == 0)? 16 : ScalingFactor[ sizeId ][ matrixId ][ x ][ y ] ScaledTransCoeff[x][y] = TransCoeffLevel[ xTbY ][ yTbY ][ cIdx ][ x ][ y ] * m * levelScale[ qP%6 ] << (qP / 6 )
Inverse transform: please refer to the attached spreadsheet; the value cannot be expressed associated with block size.
  The complexity of inverse transform is assessed according to reference software, that is, partial butterfly is applied. After this process, Resiblock, residual of each pixel, is obtained.
Block reconstruction: N2 additions
  For 0 <= x, y < N Recblock [ x ][ y ] = predSamples[ x ][ y ] + Resiblock[ x ][ y ]

## Slide 17: Number of operations - De-quantization and inverse transform
Storage requirement
  LUT of scaling factor (ScalingFactor): MN8 + 68
  One MN block which is recorded the scaling factor for each pixel. Bit-width of scaling factor is 8-bit.
  level scale (levelScale): one storage with six contents. Bit-width of each content is 8-bit.
Data transfer rate
  LUT of scaling factor (ScalingFactor): MN8
  One MN block which is recorded the scaling factor for each pixel. Bit-width of scaling factor is 8-bit.