## Slide 1
AHG5: Coding results for flexible coding order (FCO)
((JCT3V-I0116)
July 2014
LG Electronics
Junghak Nam (junghak.nam@lge.com)

## Slide 2: Introduction
Background
  Flexible coding order (FCO) scheme is only available in a software
  The draft text is implicitly designed for a texture-first coding order
  A depth-first coding gain might be potentially increased by exploiting collocated depth information like the texture-first coding is doing using texture information in the same view
Proposed method
  To support FCO functionality in 3D-HEVC
    Bug fixes and software modification for checking the corresponding texture
    Text modification for selecting an adaptive depth reference by coding order
Crosscheck
  JCT3V-I0182 (by NTT)

## Slide 3: Proposed method
Modifications to support FCO
Tool | Software modification | Text modification
MPI | 1) For dependant depth coding, mpi_flag[layerId] in VPS sets to 0 specifies that motion parameter inheritance is not used. 2) Checking process to determine whether the corresponding texture for MPI tool is available or not | 
DDD | 1) Checking process to determine whether the corresponding texture for DDD tool is available or not. | 1) Add ddd_flag[layerId] syntax element in VPS. ddd_flag[layerId] equal to 0 specifies disparity derived depth coding is not used for the layer with nuh_layer_id equal to layerId.
DMM4 | 1) Fix a compile error | 
QTL/PC | 1) For dependant depth coding, QTL/PC flag in SPS sets to 0 specifies that quad-tree limitation is not used. Note: QTL/PC syntax elements in SPS will be moved to VPS. 2) Checking process to determine whether the corresponding texture for QTL/PC is available or not. | 
DoNBDV/VSP | No changes | 1) Checking process to determine whether collocated depth is used or base depth is used
DBBP | 1) Bug fix to get virtual depth block from a co-located block position in a LCU instead of a top-left position of a LCU. | 
Cam Param | 1) Camera parameters are transmitted in depth picture, and a texture picture inherits camera parameters from the depth picture of the same view. | 

## Slide 4: Test conditions
The proposed method is integrated on 3D-HTM 11.0
To be coded Reference |  |  | HTM-11.0 |  | Test 1 |  | Test 2 |  | Test 3 |  | Test 4 |  | Test 5 | 
 |  |  | Base view | Depend. view | Base view | Depend. view | Base view | Depend. view | Base view | Depend. view | Base view | Depend. view | Base view | Depend. view
Depth coding Tool | MPI, DMM4, QTL/PC | Base texture |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Collocated texture |  |  |  | x |  | x |  | x |  | x |  | x
 | DDD | Base texture |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Collocated texture |  |  |  | x |  | x |  | x |  | x |  | x
Texture coding tool | DoNBDV | Base depth |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Collocated depth |  |  |  |  |  |  |  |  |  |  |  | 
 | VSP | Base depth |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Collocated depth |  |  |  |  |  |  |  |  |  |  |  | 
 | DBBP | Base depth |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Collocated depth |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 5: Test 1 vs. HTM-11.0
Base FCO
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.05% | 0.00% | 0.01% | 1.66% | 0.28% | 135.4% | 93.9% | 101.6%
Kendo | 0.00% | 0.05% | 0.00% | 0.01% | 2.10% | 1.02% | 136.9% | 97.8% | 100.4%
Newspaper_CC | 0.00% | 0.05% | 0.00% | 0.01% | 2.18% | 0.44% | 139.2% | 90.2% | 98.7%
GT_Fly | 0.00% | -0.93% | -1.99% | -0.25% | 1.92% | 1.91% | 138.4% | 95.5% | 97.4%
Poznan_Hall2 | 0.00% | 0.05% | 0.00% | 0.01% | 2.72% | 1.65% | 154.5% | 97.1% | 98.1%
Poznan_Street | 0.00% | 0.03% | 0.00% | 0.00% | 1.68% | 1.63% | 147.1% | 95.1% | 97.0%
Undo_Dancer | 0.00% | 0.02% | 0.00% | 0.00% | 1.84% | 1.43% | 140.2% | 96.9% | 96.7%
Shark | 0.00% | -0.84% | -1.91% | -0.23% | 2.94% | 2.09% | 142.4% | 93.8% | 94.7%
1024x768 | 0.00% | 0.05% | 0.00% | 0.01% | 1.98% | 0.58% | 137.2% | 94.0% | 100.2%
1920x1088 | 0.00% | -0.33% | -0.78% | -0.09% | 2.22% | 1.74% | 144.5% | 95.7% | 96.8%
average | 0.00% | -0.19% | -0.49% | -0.06% | 2.13% | 1.31% | 141.8% | 95.0% | 98.1%

## Slide 6: Test 2 vs. HTM-11.0
Base FCO + DoNBDV using collocated depth
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.13% | -0.54% | -0.10% | 1.56% | 0.17% | 135.0% | 90.8% | 102.0%
Kendo | 0.00% | -0.42% | -0.80% | -0.24% | 1.88% | 0.81% | 136.2% | 96.9% | 100.5%
Newspaper_CC | 0.00% | -0.51% | -0.96% | -0.28% | 1.93% | 0.25% | 138.7% | 91.6% | 98.9%
GT_Fly | 0.00% | -1.34% | -2.40% | -0.33% | 1.85% | 1.86% | 138.2% | 94.1% | 97.2%
Poznan_Hall2 | 0.00% | 0.01% | -0.71% | -0.13% | 2.60% | 1.60% | 154.2% | 97.6% | 98.4%
Poznan_Street | 0.00% | -0.18% | -0.16% | -0.08% | 1.60% | 1.57% | 146.9% | 94.7% | 96.9%
Undo_Dancer | 0.00% | -0.20% | -0.87% | -0.18% | 1.66% | 1.27% | 140.6% | 95.1% | 96.3%
Shark | 0.00% | -2.19% | -4.62% | -0.66% | 2.54% | 1.73% | 142.7% | 93.1% | 96.0%
1024x768 | 0.00% | -0.27% | -0.76% | -0.21% | 1.79% | 0.41% | 136.6% | 93.1% | 100.5%
1920x1088 | 0.00% | -0.78% | -1.75% | -0.27% | 2.05% | 1.61% | 144.5% | 94.9% | 97.0%
average | 0.00% | -0.59% | -1.38% | -0.25% | 1.95% | 1.16% | 141.5% | 94.3% | 98.3%

## Slide 7: Test 3 vs. HTM-11.0
Base FCO + VSP using collocated depth
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | -0.28% | -0.65% | -0.18% | 1.48% | 0.10% | 135.5% | 90.9% | 98.6%
Kendo | 0.00% | -0.42% | -0.61% | -0.21% | 1.90% | 0.85% | 136.9% | 93.8% | 99.5%
Newspaper_CC | 0.00% | -0.47% | -0.51% | -0.19% | 2.01% | 0.30% | 138.8% | 87.5% | 98.5%
GT_Fly | 0.00% | -1.59% | -2.87% | -0.39% | 1.79% | 1.74% | 138.2% | 94.9% | 99.4%
Poznan_Hall2 | 0.00% | 0.15% | -0.50% | -0.05% | 2.67% | 1.62% | 154.1% | 93.1% | 99.2%
Poznan_Street | 0.00% | -0.07% | -0.47% | -0.10% | 1.58% | 1.49% | 147.0% | 96.1% | 99.2%
Undo_Dancer | 0.00% | -1.17% | -1.90% | -0.38% | 1.48% | 1.01% | 139.7% | 94.5% | 98.4%
Shark | 0.00% | -3.01% | -5.38% | -0.78% | 2.43% | 1.53% | 142.1% | 94.7% | 98.5%
1024x768 | 0.00% | -0.39% | -0.59% | -0.19% | 1.80% | 0.41% | 137.1% | 90.8% | 98.8%
1920x1088 | 0.00% | -1.14% | -2.22% | -0.34% | 1.99% | 1.48% | 144.2% | 94.7% | 98.9%
average | 0.00% | -0.86% | -1.61% | -0.28% | 1.92% | 1.08% | 141.6% | 93.2% | 98.9%

## Slide 8: Test 4 vs. HTM-11.0
Base FCO + DBBP using collocated depth
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | -0.32% | -0.04% | -0.05% | 1.61% | 0.20% | 135.6% | 94.9% | 98.7%
Kendo | 0.00% | -0.17% | -0.07% | -0.04% | 2.06% | 0.97% | 137.0% | 98.8% | 99.7%
Newspaper_CC | 0.00% | -0.24% | -0.20% | -0.09% | 2.09% | 0.37% | 134.0% | 95.3% | 98.4%
GT_Fly | 0.00% | -1.10% | -2.38% | -0.31% | 1.86% | 1.86% | 137.3% | 95.0% | 98.8%
Poznan_Hall2 | 0.00% | 0.22% | -0.16% | 0.00% | 2.70% | 1.65% | 153.2% | 96.7% | 98.7%
Poznan_Street | 0.00% | -0.01% | -0.11% | -0.04% | 1.64% | 1.60% | 146.4% | 94.4% | 98.3%
Undo_Dancer | 0.00% | -1.04% | -1.84% | -0.37% | 1.49% | 1.06% | 139.7% | 95.7% | 97.6%
Shark | 0.00% | -1.77% | -3.42% | -0.48% | 2.70% | 1.88% | 141.2% | 93.4% | 96.0%
1024x768 | 0.00% | -0.24% | -0.11% | -0.06% | 1.92% | 0.51% | 135.5% | 96.3% | 98.9%
1920x1088 | 0.00% | -0.74% | -1.58% | -0.24% | 2.08% | 1.61% | 143.6% | 95.1% | 97.9%
average | 0.00% | -0.55% | -1.03% | -0.17% | 2.02% | 1.20% | 140.6% | 95.5% | 98.3%

## Slide 9: Test 5 vs. HTM-11.0
Base FCO + DoNBDV, VSP, and DBBP using collocated depth
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | -0.08% | -0.96% | -0.19% | 1.48% | 0.06% | 136.2% | 89.9% | 98.5%
Kendo | 0.00% | -0.48% | -0.70% | -0.23% | 1.89% | 0.81% | 137.5% | 92.7% | 98.7%
Newspaper_CC | 0.00% | -0.75% | -1.13% | -0.33% | 1.90% | 0.18% | 134.2% | 89.9% | 97.9%
GT_Fly | 0.00% | -1.28% | -2.64% | -0.32% | 1.86% | 1.74% | 138.2% | 95.8% | 97.9%
Poznan_Hall2 | 0.00% | 0.47% | -0.55% | -0.02% | 2.69% | 1.63% | 153.4% | 97.1% | 98.2%
Poznan_Street | 0.00% | 0.02% | -0.25% | -0.03% | 1.64% | 1.51% | 146.8% | 95.5% | 98.0%
Undo_Dancer | 0.00% | -1.79% | -3.44% | -0.67% | 1.20% | 0.76% | 139.9% | 96.4% | 98.2%
Shark | 0.00% | -3.22% | -6.19% | -0.90% | 2.31% | 1.44% | 142.3% | 94.2% | 95.3%
1024x768 | 0.00% | -0.44% | -0.93% | -0.25% | 1.76% | 0.35% | 136.0% | 90.8% | 98.3%
1920x1088 | 0.00% | -1.16% | -2.61% | -0.39% | 1.94% | 1.42% | 144.1% | 95.8% | 97.5%
average | 0.00% | -0.89% | -1.98% | -0.34% | 1.87% | 1.02% | 141.1% | 93.9% | 97.8%

## Slide 10: Conclusion
Summary of tests
  Coding performance of texture coding tools are improved by FCO consistently
  Synthesized PSNR of FCO is degraded by disabling MPI and using VSO with un-coded texture
Conclusion
  This contribution proposes to support FCO in 3D-HEVC
  Decoder can be aware of a more accurate depth reference according to coding order
  It is recommended to include the proposed method to the next 3D-HEVC
 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Test-1 FCO | -0.06% | 2.13% | 1.31%
Test-2 FCO + DoNBDV | -0.25% | 1.95% | 1.16%
Test-3 FCO + VSP | -0.28% | 1.92% | 1.08%
Test-4 FCO + DBBP | -0.17% | 2.02% | 1.20%
Test-5 FCO + DoNBDV + DBBP + VSP | -0.34% | 1.87% | 1.02%