## Slide 1
CE2 related: Reduction of the number of
intra prediction modes for depth coding
(JCT3V-I0117)
July 2014
LG Electronics
Jin Heo (jin78.heo@lge.com)
JungHak Nam (junghak.nam@lge.com)
Sehoon Yea (sehoon.yea@lge.com)

## Slide 2: Introduction
Current 3D-HTM intra coding
  Use 35 intra prediction modes for both texture and depth intra coding
Problem of conventional intra coding
  Different characteristics of texture and depth videos
  Depth video: 1) little variation within a block 2) simple or smooth regions
  35 intra prediction modes are unnecessarily expensive for depth intra coding
Proposed method
  Reduce the number of conventional intra prediction modes for depth intra coding
Crosscheck
  I0179 (by NTT)

## Slide 3: Proposed Method
Use 11 intra prediction modes for depth intra coding
<Conventional 35 intra prediction modes for depth >
<Proposed 11 intra prediction modes for depth >

## Slide 4: Experimental Results
CTC
AI

## Slide 5: Conclusion
Proposed method
  Reduce the number of intra prediction modes for depth intra coding
Performance
  0.0% and -0.2% coding gains under common test condition (CTC) and all-intra configuration (AI), respectively with negligible encoding/decoding complexity