## Slide 1
CE2: Advanced Boundary Chain(ABC)
coding for depth intra coding
(JCT3V-I0118)
July 2014

## Slide 2: CABAC throughput aspect
Texture and depth will be likely to be processed in a parallel manner
- Texture coding will be the critical-path that determines throughput
- CABAC bins for depth coding estimated to be 14% of total (texture+depth)
Even when texture and depth are decoded in a serial manner
- Chain coding adds only 1% to the total number of bins (out of 14%)
Ratio of context coded bins for ABC mode (%) (bins for ABC / Total bins)
  Average ratio of context coded bins for ABC : 1.23
<number>
Balloons | GT_Fly | Kendo | Newspaper | Poznan_Hall2 | Poznan_Street | Shark | Undo_Dancer
1.07 | 0.88 | 1.80 | 1.59 | 0.60 | 1.59 | 1.52 | 0.82

## Slide 3: Context coded bins in size of 8x8 block for ABC
Worst case
  Chain coding with 4x4 block
  A number of edge_code can have 2N (=8)
  Context coded bins/pixel for a 4x4 block: 1.455
  Maximum number of context coded bins of a 8x8 block for ABC: 93.12
<number>
Syntax element | maximum context-coded bins
edge_start_side | 2
edge_start_position | bypass
num_edge_codes | 4
edge_code | 2.16 * 8 = 17.28
Total | 23.28
0.710 * 2 + 0.13 * 2 + 0.145 * 2 + 0.012 * 3 + 0.003 * 3 = 2.16
Symbol | edge_code | probability
0° | 00 | 0.710
45° | 01 | 0.130
-45° | 10 | 0.145
90° | 110 | 0.012
-90° | 111 | 0.003

## Slide 4: Context coded bins in size of 8x8 block for ABC
Actual maximum number of context coded bins in 8x8 blocks
  Maximum number of context coded bins for ABC: 42
Average number of context coded bins in 8x8 blocks
  Average number of context coded bins for ABC: 17.97
<number>
Balloons | GT_Fly | Kendo | Newspaper | Poznan_Hall2 | Poznan_Street | Shark | Undo_Dancer
36 | 42 | 35 | 40 | 32 | 42 | 42 | 37
Balloons | GT_Fly | Kendo | Newspaper | Poznan_Hall2 | Poznan_Street | Shark | Undo_Dancer
17.71 | 18.46 | 17.79 | 18.26 | 17.63 | 18.26 | 17.97 | 17.99