## Slide 1
Page <number>
Remove “depth_dc_flag” signalling in DMM cases
Xu Chen, Xiaozhen Zheng, Yongbin Lin and Jianhua Zheng
Notes: 26/7/31
<number>

## Slide 2: Summary
Page <number>
  Current 3D-HEVC, “depth_dc_flag” need to be signalled in both DMM and SDC DMM cases. In SDC DMM cases, “depth_dc_flag” value depends on the residual value of segments. In DMM cases, “depth_dc_flag” value depends on weather dc offset is exist or not.
  where
  dcOffsetAvailFlag = ( !sdc_flag[ xTb ][ yTb ] && depth_dc_flag[xTb][yTb] )

## Slide 3: Proposed
Page <number>

## Slide 4: Result
Page <number>
HTM11 Test condition: CTC
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% | 99.5% | 114.0% | 101.7%
Kendo | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | -0.1% | 99.3% | 102.1% | 102.5%
Newspaper_CC | 0.0% | -0.1% | 0.2% | 0.0% | 0.1% | -0.1% | 99.3% | 88.5% | 101.1%
GT_Fly | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 99.3% | 92.4% | 99.5%
Poznan_Hall2 | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 99.4% | 98.3% | 103.1%
Poznan_Street | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 99.6% | 105.0% | 101.0%
Undo_Dancer | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 99.5% | 112.7% | 101.1%
Shark | 0.0% | -0.2% | 0.1% | 0.0% | 0.0% | 0.0% | 99.0% | 91.7% | 101.3%
1024x768 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | -0.1% | 99.4% | 101.5% | 101.8%
1920x1088 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 99.4% | 100.0% | 101.2%
average | 0.00% | -0.04% | 0.01% | 0.00% | -0.01% | -0.02% | 99.4% | 100.6% | 101.4%

## Slide 5: Result
Page <number>
HTM11 Test condition: AI
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 96.9% | 102.3% | 101.9%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 97.0% | 103.4% | 103.3%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 96.0% | 105.1% | 105.3%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 96.7% | 101.0% | 106.8%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 97.0% | 101.8% | 102.2%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 96.3% | 101.5% | 101.7%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 96.2% | 98.8% | 102.1%
Shark | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 97.0% | 99.0% | 101.2%
1024x768 | 0.00% | 0.00% | 0.00% | 0.00% | -0.01% | -0.01% | 96.6% | 103.6% | 103.5%
1920x1088 | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 96.6% | 100.4% | 102.8%
average | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 96.6% | 101.6% | 103.1%

## Slide 6: Conclusions
Page <number>
depth_dc_flag is removed in DMM process.
Fewer restrictions for SDC DMM checking.
Fewer DMM cases need to check in encoder side.
0.02 bit-saving for synthesized views on CTC.
Suggest to be adopted.
Thanks for cross-check by Qualcomm

## Slide 7
Page <number>
Thank you!
www.hisilicon.com