## Slide 1
www.hisilicon.com
The Right silicon for your next BIG idea
Bug-fixing of depth-based block partitioning signaling
Yongbing Lin1, Jianhua Zheng1,
Xin Wang2, Ce Zhu2
JCT3V-I0125
1. HiSilicon Technologies 2. UESTC

## Slide 2: Summary
The proposal is to fix a bug regarding on the condition of DBBP flag signaling. To restrict the DBBP flag to be transmitted for Part_2NxN and Part_Nx2N mode.
Implemented based on HTM11.0, results of CTC and AI configurations,
-0.06% bit-saving on synthesized views in All-Intra configurations
-0.01% bit-saving on synthesized views in CTC,
Thanks Sharp for cross-checking (JCT3V-I0163)

## Slide 3: Problem
The DBBP flag is signaled depending on a condition that the coding CU block should not be coded with intra mode. The DBBP flag is still signaled even when the block is coded in inter mode with other kinds of partition modes.

## Slide 4: Proposed method
The DBBP flag will be signaled when the block partition mode is 2NxN or Nx2N.

## Slide 5: Experimental results
Page 5
  Implemented based on HTM11.0

## Slide 6: Experimental results
Page 6
  Implemented based on HTM11.0

## Slide 7: Conclusions
Propose to restrict the DBBP flag to be transmitted for Part_2NxN and Part_Nx2N mode.
Suggest to adopt the DBBP bug-fixing method.

## Slide 8
Thank you!
www.hisilicon.com