## Slide 1: Simplification of VSP candidate derivation (JCT3V-I0130)
ETRI* and KHU
*Gun Bang, Min Seong Lee, Young Su Heo, Gwang Hoon Park, *Gwang Soon Lee, *Nam Ho Hur

## Slide 2: Introduction
In the current HTM, the inherited VSP candidates are derived from all of the spatial neighboring blocks
The current NBDV process derives DV from the first available block between left and above block
However, all of these candidates have the same DV with the current CU
There is no benefit to use multiple inherited VSP candidates

## Slide 3: Proposal
Method 1. Skipping for derivation process for default VSP merging candidate
  If one or more of the inherited VSP candidate is available, derivation process for default VSP merging candidate can be skipped
Method 2. Constraint position of inherited VSP candidates
  5 blocks → 2 blocks (Left, Above)
  The first available block is selected as the inherited VSP candidates, and skip derivation process for default VSP candidate
  If available inherited VSP candidate does not exist, then default VSP candidate derivation process is performed

## Slide 4: Proposal

## Slide 5: Proposal
By proposed simplification, MCL could have only one VSP merging candidate with no redundancy

## Slide 6: Result
Default VSP Derivation Skip

## Slide 7: Result
Limit inheritance VSP cand. Position + default VSP skip

## Slide 8: Conclusion
In the method 1, Skipping derivation process of default VSP merging candidate are proposed when at lease one inherited VSP candidates is available.
  The coding gain is -0.01% in total BD-Rate
  By this proposed method, the number of derivation process can be reduced
In the method 2, the positions of inherited VSP candidate are constrained to two (A1, B1) blocks
  The available one of A1 and B1 is used by the inherited VSP and then default VSP candidate process can be skipped.
  The coding gain is -0.02% in total BD-Rate
  As a benefit,
    The memory access rate related with VSP flag can be reduced
    The number of derivation process decreases. and redundant candidates in MCL are removed.
Thank you for Zhejiang University’s cross-checking(JCT3V-I0174)