## Slide 1: JCT3V-I0131 Adaptive Candidate Selection (ACS)
Notes: <number>

## Slide 2: Motivation
When merge mode is invoked, IVMC or MPI candidate is frequently selected for dependent texture view or depth, respectively.
For dependent texture view, if temporal collocated block used the IVMC for merge mode, the best candidate for the merge mode in current block is also IVMC in most case.
For depth map, if temporal collocated block used the MPI for merge mode, the best candidate for the merge mode in current block is also MPI in most case.
Signaling the merging index can be omitted by exploiting such relationship in terms of candidate selection.
Therefore, the adaptive candidate selection method is proposed.

## Slide 3: Proposal
Condition 1 for dependent texture view
    Current PU is belong to the dependent view
    Temporal collocated PU used IVMC for the merge mode
    IVMC is available for the current PU.
If the condition 1 is true,
  IVMC is forced to set to be used for the merge mode.
Condition 2 for depth
  Current PU is belong to the depth-map
  Temporal collocated PU used MPI for the merge mode
  MPI is available for the current PU.
If the condition 2 is true,
  MPI is forced to set to be used for the merge mode.
Otherwise, the existing process for the merge mode is applied.
Notes: <number>

## Slide 4: The example of proposed
Example of two conditions for adaptive candidate selection
PUCur
PUCol
IVMC is used
POC = 6 (B_SLICE)
POC = 7
Condition 1
Dependent view
PUCur
PUCol
MPI is used
POC = 6 (B_SLICE)
POC = 7
Condition 2
Depth map
MCL = { IVMC, ... ... }
MCL = { MPI, ... ... }
Notes: <number>

## Slide 5: The proposed flowchart
Flow chart of the proposed method
layerId != 0
VpsDepthFlag[ layerId ]
mpi_flag[ nuh_layer_id ] && colMergType = = T && T is available
iv_mv_pred_flag[ nuh_layer_id ] && colMergType = = IvMC && IvMC is available
1
1
1
decode merging index
End
1
Start
Set merging index to 0
Notes: <number>

## Slide 6: Results
HTM11.0 vs proposed method (DBBP off)
The proposed method is only applied to 2Nx2N PUs.
The simulation is performed without DBBP due to bug in terms of implementation.
Synthesis result is decreased(0.23%) due to the DDD candidate.
  In ACS condition, DDD is selected as the best candidate for depth coding (about 1%) .
Notes: <number>

## Slide 7: Conclusion
The proposed method is only applied to 2Nx2N PUs.
  In decoder side, the status of each PU in merge candidate index symbol is saved in order to be utilized for deciding merge candidate(IVMC or MPI) in the current PU.
-0.15% coding gain in total BDR.
The benefits are the following as
  It’s not necessary that Merging index is signaled.
  Operations and memory bandwidth can be reduced for parallel derivation of merging candidates.
     Since the process for deriving the other candidates and MCL construction can be omitted.
Recommend to adopt in HTM.
Thank you for Samsung’s cross-checking(JCT3V-I0149)
Notes: <number>