## Slide 1: Depth Intra Skip Coding (DISC) Mode (J0038)
Single depth mode reconstructs a CU with one single depth value (SDV), which is derived from neighboring pixels (I0095)
Single depth mode needs the SDV list contruction and pruning processes
Proposed method uses the existing intra prediciton mode (vertical and horizontal) instead of the SDV derivation
In the 4th JCT-3V meeting, the recontruction of the SDC mode was changed from Reconx,y=DC(Predx,y)+DC(Resx,y) into Reconx,y=Predx,y+DC(Resx,y)
  Adopted from D0110/D0136 (-0.2% gain)
vertical
horizontal
Reconx,y = SDV
Reconx,y = Predx,y

## Slide 2: Result
CTC
All Intra
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | -0.11% | 0.06% | 0.00% | -0.11% | -0.14% | 100.1% | 102.1% | 103.1%
Kendo | 0.00% | -0.15% | 0.20% | 0.04% | -0.17% | -0.36% | 99.4% | 96.0% | 101.5%
Newspaper_CC | 0.00% | 0.11% | 0.14% | 0.02% | -0.17% | -0.20% | 99.8% | 98.2% | 100.3%
GT_Fly | 0.00% | 0.03% | 0.08% | 0.01% | -0.10% | -0.04% | 99.5% | 94.0% | 94.9%
Poznan_Hall2 | 0.00% | 0.06% | -0.03% | 0.00% | -0.75% | -1.05% | 101.2% | 94.1% | 101.7%
Poznan_Street | 0.00% | 0.13% | 0.07% | 0.03% | 0.01% | -0.01% | 99.8% | 105.1% | 99.7%
Undo_Dancer | 0.00% | -0.30% | -0.31% | -0.08% | -0.24% | -0.36% | 100.1% | 106.9% | 102.7%
Shark | 0.00% | 0.02% | 0.11% | 0.02% | 0.07% | 0.14% | 100.2% | 100.8% | 103.2%
1024x768 | 0.00% | -0.05% | 0.13% | 0.02% | -0.15% | -0.23% | 99.7% | 98.8% | 101.6%
1920x1088 | 0.00% | -0.01% | -0.02% | 0.00% | -0.20% | -0.26% | 100.2% | 100.2% | 100.4%
average | 0.00% | -0.03% | 0.04% | 0.01% | -0.18% | -0.25% | 100.0% | 99.6% | 100.9%
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.00% | 0.00% | 0.00% | -0.18% | -0.12% | 99.4% | 100.2% | 100.6%
Kendo | 0.00% | 0.00% | 0.00% | 0.00% | -0.28% | -0.30% | 97.2% | 100.4% | 101.1%
Newspaper_CC | 0.00% | 0.00% | 0.00% | 0.00% | -0.17% | -0.11% | 100.0% | 98.5% | 103.8%
GT_Fly | 0.00% | 0.00% | 0.00% | 0.00% | -0.15% | 0.06% | 100.3% | 99.3% | 100.8%
Poznan_Hall2 | 0.00% | 0.00% | 0.00% | 0.00% | -0.80% | -0.64% | 99.7% | 99.8% | 103.3%
Poznan_Street | 0.00% | 0.00% | 0.00% | 0.00% | -0.12% | 0.00% | 99.8% | 99.6% | 97.2%
Undo_Dancer | 0.00% | 0.00% | 0.00% | 0.00% | -0.26% | -0.19% | 98.5% | 98.5% | 100.1%
Shark | 0.00% | 0.00% | 0.00% | 0.00% | 0.06% | 0.27% | 100.7% | 99.2% | 98.0%
1024x768 | 0.00% | 0.00% | 0.00% | 0.00% | -0.21% | -0.17% | 98.9% | 99.7% | 101.8%
1920x1088 | 0.00% | 0.00% | 0.00% | 0.00% | -0.25% | -0.10% | 99.8% | 99.3% | 99.9%
average | 0.00% | 0.00% | 0.00% | 0.00% | -0.24% | -0.13% | 99.4% | 99.4% | 100.6%
The proposed method achieves the bit saving of about -0.2% (-1.1% in Poznan_Hall2), reduce the complexity, and remove the SDV derivation part (I.8.4.4.2.9) in WD

## Slide 3: Additional Result
Singe Depth Mode
DISC Mode
Anchor : HTM 12.0 – Single Depth Mode (All intra condition)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.00% | 0.00% | 0.00% | -0.12% | -0.22% | 94.7% | 96.5% | 101.7%
Kendo | 0.00% | 0.00% | 0.00% | 0.00% | -0.15% | -0.25% | 95.5% | 93.1% | 99.8%
Newspaper_CC | 0.00% | 0.00% | 0.00% | 0.00% | -0.14% | -0.28% | 96.0% | 94.4% | 97.3%
GT_Fly | 0.00% | 0.00% | 0.00% | 0.00% | -0.51% | -0.76% | 89.8% | 87.8% | 97.1%
Poznan_Hall2 | 0.00% | 0.00% | 0.00% | 0.00% | -0.27% | -0.26% | 84.0% | 83.6% | 89.1%
Poznan_Street | 0.00% | 0.00% | 0.00% | 0.00% | -0.23% | -0.35% | 94.9% | 96.3% | 101.9%
Undo_Dancer | 0.00% | 0.00% | 0.00% | 0.00% | 0.02% | -0.03% | 92.1% | 100.4% | 99.2%
Shark | 0.00% | 0.00% | 0.00% | 0.00% | -0.29% | -0.54% | 94.0% | 94.1% | 100.1%
1024x768 | 0.00% | 0.00% | 0.00% | 0.00% | -0.14% | -0.25% | 95.4% | 94.7% | 99.6%
1920x1088 | 0.00% | 0.00% | 0.00% | 0.00% | -0.26% | -0.39% | 91.0% | 92.4% | 97.5%
average | 0.00% | 0.00% | 0.00% | 0.00% | -0.21% | -0.33% | 92.6% | 93.3% | 98.3%
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.00% | 0.00% | 0.00% | -0.30% | -0.34% | 94.2% | 96.7% | 102.4%
Kendo | 0.00% | 0.00% | 0.00% | 0.00% | -0.44% | -0.55% | 92.8% | 93.5% | 100.8%
Newspaper_CC | 0.00% | 0.00% | 0.00% | 0.00% | -0.31% | -0.38% | 96.0% | 93.0% | 100.9%
GT_Fly | 0.00% | 0.00% | 0.00% | 0.00% | -0.67% | -0.70% | 90.0% | 87.2% | 97.9%
Poznan_Hall2 | 0.00% | 0.00% | 0.00% | 0.00% | -1.07% | -0.90% | 83.7% | 83.4% | 92.0%
Poznan_Street | 0.00% | 0.00% | 0.00% | 0.00% | -0.35% | -0.35% | 94.7% | 96.0% | 99.1%
Undo_Dancer | 0.00% | 0.00% | 0.00% | 0.00% | -0.24% | -0.22% | 90.7% | 98.8% | 99.3%
Shark | 0.00% | 0.00% | 0.00% | 0.00% | -0.23% | -0.28% | 94.6% | 93.4% | 98.1%
1024x768 | 0.00% | 0.00% | 0.00% | 0.00% | -0.35% | -0.42% | 94.4% | 94.4% | 101.4%
1920x1088 | 0.00% | 0.00% | 0.00% | 0.00% | -0.51% | -0.49% | 90.8% | 91.8% | 97.3%
average | 0.00% | 0.00% | 0.00% | 0.00% | -0.45% | -0.46% | 92.1% | 92.8% | 98.8%

## Slide 4: Additional Result
Singe Depth Mode
DISC Mode
Anchor : HTM 12.0 – Single Depth Mode (CTC)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.12% | 0.03% | 0.03% | -0.01% | -0.07% | 101.2% | 96.1% | 100.3%
Kendo | 0.00% | 0.08% | -0.19% | -0.05% | -0.26% | -0.43% | 96.8% | 95.7% | 95.0%
Newspaper_CC | 0.00% | -0.08% | -0.19% | -0.03% | -0.08% | -0.22% | 99.9% | 99.6% | 100.6%
GT_Fly | 0.00% | 0.13% | 0.30% | 0.06% | -0.27% | -0.64% | 101.8% | 97.3% | 102.0%
Poznan_Hall2 | 0.00% | 0.11% | -0.21% | 0.00% | -0.12% | -0.34% | 101.6% | 99.8% | 99.4%
Poznan_Street | 0.00% | 0.17% | 0.00% | 0.03% | -0.07% | -0.12% | 103.1% | 97.0% | 101.9%
Undo_Dancer | 0.00% | 0.42% | 0.11% | 0.08% | 0.08% | 0.07% | 101.0% | 92.1% | 97.7%
Shark | 0.00% | -0.02% | -0.19% | -0.01% | -0.13% | -0.31% | 101.3% | 96.9% | 98.9%
1024x768 | 0.00% | 0.04% | -0.12% | -0.02% | -0.11% | -0.24% | 99.3% | 97.1% | 98.6%
1920x1088 | 0.00% | 0.16% | 0.00% | 0.03% | -0.10% | -0.27% | 101.8% | 96.6% | 100.0%
average | 0.00% | 0.12% | -0.04% | 0.01% | -0.11% | -0.26% | 100.8% | 96.8% | 99.5%
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.01% | 0.08% | 0.03% | -0.11% | -0.22% | 101.3% | 98.1% | 103.4%
Kendo | 0.00% | -0.07% | 0.01% | 0.00% | -0.43% | -0.79% | 96.2% | 91.9% | 96.4%
Newspaper_CC | 0.00% | 0.03% | -0.05% | -0.01% | -0.24% | -0.42% | 99.7% | 97.8% | 100.8%
GT_Fly | 0.00% | 0.16% | 0.38% | 0.07% | -0.36% | -0.68% | 101.3% | 93.4% | 96.8%
Poznan_Hall2 | 0.00% | 0.17% | -0.24% | -0.01% | -0.87% | -1.39% | 102.8% | 93.9% | 101.1%
Poznan_Street | 0.00% | 0.30% | 0.07% | 0.06% | -0.06% | -0.14% | 102.9% | 91.1% | 101.6%
Undo_Dancer | 0.00% | 0.11% | -0.20% | 0.00% | -0.16% | -0.29% | 101.1% | 92.1% | 100.4%
Shark | 0.00% | 0.00% | -0.08% | 0.01% | -0.06% | -0.17% | 101.5% | 97.7% | 102.0%
1024x768 | 0.00% | -0.01% | 0.01% | 0.01% | -0.26% | -0.47% | 99.1% | 95.9% | 100.2%
1920x1088 | 0.00% | 0.15% | -0.01% | 0.03% | -0.30% | -0.53% | 101.9% | 93.6% | 100.4%
average | 0.00% | 0.09% | 0.00% | 0.02% | -0.29% | -0.51% | 100.9% | 94.5% | 100.3%