## Slide 1
PU boundary deblocking restriction for DBBP blocks
(JCT3V-J0043)
Sunmi Yoo and Sehoon Yea
LG Electronics
October 2014

## Slide 2: Summary
Proposed method
  Skip deblocking on the PU boundary for DBBP blocks
  Red : contour boundary filter, yellow : deblocking filter
Result
  No significant impact on coding efficiency
  Computation saving for redundant deblocking process

## Slide 3: Experimental Result
Test S/W : HTM-12.0
As a result, it is found out that the deblocking filter for DBBP blocks has no impact on the current 3D-HEVC.
Table 1. No PU boundary deblocking for DBBP blocks vs. HTM-12.0

## Slide 4: Computational saving
Several steps to deblock PU boundary or TU boundary
  Firstly TU or PU boundary check
  Deblocking filter applied when all the conditions meet
A dashed process can be skipped.

## Slide 5: Computational saving
Bs calculation
Beta calculation
Deblocking
 | Compare | Add/Sub
Bs calculation | 31 | 12
CU size | Add/Sub | LUT access | Compare
16x16 | 184 | 2 | 80
32x32 | 736 | 2 | 320
64x64 | 2944 | 2 | 1280
CU size | Filter type | Add/Sub | Compare
16x16 | Normal filter | 136 | 72
 | Strong filter | 714 | 8
32x32 | Normal filter | 544 | 288
 | Strong filter | 1344 | 32
64x64 | Normal filter | 2176 | 1152
 | Strong filter | 5376 | 128