## Slide 1
Removal of depth_dc_flag syntax (JCT3V-J0047)
October 2014
LG Electronics
Junghak Nam (junghak.nam@lge.com)

## Slide 2: Introduction
In last meeting, depth_dc_flag was removed from DMM (JCT3V-I0120)
In current 3D-HEVC, depth_dc_flag syntax specifies that depth residual is present when a CU is coded by intra mode with SDC
 | Intra |  | Inter
 | Conventional intra | DMM | 
SDC on | depth_dc_flag depth_dc_abs depth_dc_sign_flag (Zero level disallows) | depth_dc_flag depth_dc_abs depth_dc_sign_flag (Zero level allows) | depth_dc_abs depth_dc_sign_flag (Zero level disallows)
SDC off | - | depth_dc_flag depth_dc_abs depth_dc_sign_flag (Zero level allows) | -

## Slide 3: Proposal
In order to simplify the syntax for depth residual, it is proposed to remove depth_dc_flag syntax
  DC offset calculation is also slightly modified as below:
DcOffset[ x0 ][ y0 ][ i ] = ( 1 − 2 *depth_dc_sign_flag[ x0 ][ y0 ][ i ] ) * ( depth_dc_abs[ x0 ][ y0 ][ i ] − dcNumSeg ( CuPredMode[ x0 ][ y0 ] ! = MODE_INTRA ) +2 )
 | Intra |  | Inter
 | Conventional intra | DMM | 
SDC on | depth_dc_flag depth_dc_abs depth_dc_sign_flag (Zero level allowed) | depth_dc_flag depth_dc_abs depth_dc_sign_flag (Zero level allowed) | depth_dc_abs depth_dc_sign_flag (Zero level disallowed)
SDC off | - | depth_dc_abs depth_dc_sign_flag (Zero level allowed) | -

## Slide 4: Experimental results
Anchor : HTM-12.0 under CTC
Tested : Proposed removal of depth_dc_flag

## Slide 5: Experimental results
Anchor : HTM-12.0 under AI
Tested : Proposed removal of depth_dc_flag