## Slide 1: Clipping for candidate index of single depth mode JCT3V-J0052

## Slide 2: Introduction
Single depth mode
  Reconstruction of the current CU by a single sample value
  A sample candidate list is constructed
  A candidate index is encoded to indicate the sample values for the current CU

## Slide 3: Sample candidate list generation
Filling the entry for list with 0 or 1 entry
  Offset candidate (available sample +1)
  Half dynamic range value (e.g. 128 for 8bits)
Unintended bugs on offset candidate
  It can excess the dynamic range.
  Clipping operation for the offset candidate is required.
numCand = 0 for( i = 0; i < 5; i++ ) if ( availableFlag[ i ] && numCand < 2 ) sampleCandList[ numCand++ ] = predSample[ i ] if( numCand = = 0 ) sampleCandList[ numCand++ ] = ( 1 << ( BitDepthY − 1 ) ) if( numCand = = 1 ) sampleCandList[ numCand++ ] = Clip3( 0, ( 1 << bitDepth ) − 1, sampleCandList[ 0 ] + 1)
Proposed 3D-HEVC specification for the clipping

## Slide 4: Conclusion
Single depth mode
  Single sample value is employed to fill the current CU
  depth sample value is selected in sample candidate list.
Unintended bugs can be existed.
  Offset candidate can excess the dynamic range.
  Clipping operation for the entry is required.