## Slide 1: Simplification on CABAC context for single depth mode JCT3V-J0053

## Slide 2: Summary
SDM (Single depth mode)
  Technique to efficiently code the smooth area in depth map
  Candidate index to indicate the sample values for the current CU
Removal of CABAC context for single_sample_idx
  Bypass coding of sample candidate index
  Enhanced throughput
Experimental results
  0.03%, 0.06% BD-rate loss in CTC and AI

## Slide 3: Removal of CABAC context for the syntax
Syntax for Single depth mode
  single_sample_flag
  single_sample_idx
Context models for the elements
Bypass coding of single_sample_idx
  For throughput and computational complexity
Initialization variable | ctxIdx of single_sample_idx |  | 
 | 0 | 1 | 2
initValue | 137 | 137 | 137
Initialization variable | ctxIdx of single_sample_flag |  | 
 | 0 | 1 | 2
initValue | 185 | 185 | 185
Bias to symbol ‘1’
Bias to symbol ‘0’

## Slide 4: Experimental results
The proposed method vs. HTM-12.0 in CTC
The proposed method vs. HTM-12.0 in AI
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.1% | -0.1% | -0.03% | 0.03% | 0.00% | 100.1% | 103.9% | 92.0%
Kendo | 0.0% | 0.0% | 0.2% | 0.03% | 0.10% | 0.13% | 99.7% | 96.3% | 98.7%
Newspaper_CC | 0.0% | 0.1% | 0.1% | 0.00% | -0.02% | -0.03% | 100.3% | 102.0% | 97.1%
GT_Fly | 0.0% | -0.1% | -0.4% | -0.06% | 0.07% | 0.05% | 100.6% | 101.0% | 103.5%
Poznan_Hall2 | 0.0% | -0.2% | 0.1% | 0.00% | 0.06% | 0.14% | 99.5% | 97.4% | 95.9%
Poznan_Street | 0.0% | -0.1% | 0.0% | -0.02% | 0.01% | 0.00% | 100.7% | 99.1% | 102.4%
Undo_Dancer | 0.0% | -0.1% | -0.2% | -0.03% | -0.02% | -0.10% | 99.9% | 100.7% | 91.5%
Shark | 0.0% | 0.0% | 0.0% | 0.01% | 0.09% | 0.06% | 100.3% | 96.2% | 99.5%
1024x768 | 0.0% | 0.0% | 0.0% | 0.00% | 0.04% | 0.03% | 100.0% | 100.7% | 95.9%
1920x1088 | 0.0% | -0.1% | -0.1% | -0.02% | 0.04% | 0.03% | 100.2% | 98.9% | 98.5%
average | 0.0% | -0.1% | 0.0% | -0.01% | 0.04% | 0.03% | 100.1% | 99.6% | 97.6%
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.03% | 0.03% | 98.5% | 105.0% | 116.1%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.06% | 0.04% | 97.1% | 97.0% | 111.9%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.02% | 0.00% | 99.5% | 105.3% | 111.8%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.20% | 0.17% | 101.6% | 103.7% | 99.6%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.13% | 0.09% | 96.1% | 101.8% | 108.6%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.08% | 0.06% | 100.2% | 99.7% | 93.6%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.03% | -0.01% | 96.7% | 102.3% | 109.3%
Shark | 0.0% | 0.0% | 0.0% | 0.0% | 0.14% | 0.10% | 100.0% | 103.4% | 107.4%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.04% | 0.02% | 98.4% | 102.4% | 113.3%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.12% | 0.08% | 98.9% | 102.2% | 103.7%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.09% | 0.06% | 98.7% | 102.3% | 107.3%