## Slide 1: JCT3V-J0055 Motion buffer reduction for depth
Notes: <number>

## Slide 2: Introduction
Motion compression is performed after picture and accessing unit (AU) is coded in order to reduce size of buffer for storing motion data.
In the current 3D-HEVC, same ratio for the both texture and depth is applied for motion compression.
Compared to the texture, depth motion data is rarely used for motion prediction due to the other motion candidates such as MPI.
Therefore, higher compression ratio on depth motion data can be utilized.

## Slide 3: Proposed method
Proposed unit sizes for subsampling depth motion data
Case 1, 3, 5: Immediate compression
Case 2, 4: Progressive compression
Minimum partition size is 4x4
 | After each depth is coded | After AU is coded
Anchor | 8x8 | 16x16
Case 1 | 32x32 | 32x32
Case 2 | 32x32 | 64x64 (LCU)
Case 3 | 64x64 (LCU) | 64x64 (LCU)
Case 4 | 64x64 (LCU) | 128x128 (4LCU)
Case 5 | 128x128 (4LCU) | 128x128 (4LCU)
Notes: <number>

## Slide 4: Proposed method
Proposed (immediate)
Proposed (Progressive)
Anchor
Texture motion data
Depth motion data
1/16
After all of the pictures in the same AU are coded
Texture motion data
Depth motion data
Texture motion data
Depth motion data
1/256
Proposed (Case 3)
1/256
1/64
1/4
1/16
1/4
1/16
1/4
1/16
1/4
Proposed (Case 2)
Anchor
After each picture is coded
Notes: <number>

## Slide 5: Simulation results summary
Summary results on the test cases
 | Unit size (after each depth) | Unit size(after AU) | Video 1 | Video 2 | Video PSNR / video bitrate | Video PSNR / total bitrate | Synth PSNR / total bitrate
Anchor | 8x8 | 16x16 | - | - | - | - | -
Case 1 | 32x32 | 32x32 | 0.01% | 0.02% | 0.01% | 0.01% | 0.02%
Case 2 | 32x32 | 64x64 | -0.01% | 0.00% | 0.00% | 0.01% | 0.05%
Case 3 | 64x64 | 64x64 | -0.01% | 0.00% | 0.00% | 0.03% | 0.08%
Case 4 | 64x64 | 256x256 | 0.02% | -0.01% | 0.00% | 0.04% | 0.12%
Case 5 | 256x256 | 256x256 | 0.02% | -0.01% | 0.00% | 0.06% | 0.16%
Case 3 was cross-checked by Sharp.
  0.03% and 0.08% loss on video and synthesized, respectively
Notes: <number>

## Slide 6: Conclusion
It is proposed to apply higher sampling ratio in depth motion data then texture.
The proposed method results negligible coding loss on video and synthesized BD-rate while an amount of motion buffer is reduced.
It is recommended to adopt this method in next 3D-HEVC an HTM.

## Slide 7: Simulation results: Case 1
Case 1: Immediate (1/64, 1/64)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.04% | -0.01% | 0.01% | 0.02% | 0.11% | 100.9% | 100.4% | 99.5%
Kendo | 0.00% | -0.09% | 0.08% | 0.01% | 0.03% | 0.01% | 99.8% | 99.6% | 99.6%
Newspaper_CC | 0.00% | -0.03% | -0.02% | -0.01% | -0.02% | -0.05% | 98.9% | 100.0% | 99.5%
GT_Fly | 0.00% | 0.09% | 0.09% | 0.01% | 0.01% | -0.01% | 100.3% | 100.7% | 99.8%
Poznan_Hall2 | 0.00% | 0.11% | 0.07% | 0.03% | 0.04% | 0.00% | 100.7% | 100.9% | 100.0%
Poznan_Street | 0.00% | 0.01% | 0.04% | 0.00% | 0.01% | 0.02% | 99.8% | 99.5% | 99.6%
Undo_Dancer | 0.00% | -0.08% | -0.05% | -0.02% | 0.00% | 0.02% | 100.3% | 98.5% | 99.8%
Shark | 0.00% | 0.07% | 0.00% | 0.01% | 0.01% | 0.04% | 100.4% | 100.3% | 100.1%
1024x768 | 0.00% | -0.03% | 0.02% | 0.00% | 0.01% | 0.02% | 99.9% | 100.0% | 99.5%
1920x1088 | 0.00% | 0.04% | 0.03% | 0.01% | 0.01% | 0.01% | 100.3% | 100.0% | 99.9%
average | 0.00% | 0.01% | 0.02% | 0.01% | 0.01% | 0.02% | 100.1% | 100.0% | 99.7%
Notes: <number>

## Slide 8: Simulation results: Case 2
Case 2: Progressive (1/64, 1/256)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.07% | -0.02% | 0.00% | 0.02% | 0.13% | 100.2% | 101.2% | 100.0%
Kendo | 0.00% | -0.11% | 0.03% | 0.00% | 0.02% | 0.03% | 98.7% | 99.6% | 99.6%
Newspaper_CC | 0.00% | -0.04% | -0.01% | -0.01% | -0.01% | -0.07% | 98.9% | 100.4% | 100.0%
GT_Fly | 0.00% | -0.02% | -0.07% | -0.01% | 0.00% | 0.00% | 101.7% | 101.3% | 99.9%
Poznan_Hall2 | 0.00% | 0.10% | 0.02% | 0.01% | 0.00% | 0.14% | 100.4% | 98.4% | 99.7%
Poznan_Street | 0.00% | 0.01% | -0.02% | 0.00% | 0.02% | 0.02% | 100.0% | 99.4% | 99.8%
Undo_Dancer | 0.00% | -0.01% | 0.02% | 0.00% | 0.02% | 0.10% | 99.2% | 99.2% | 100.0%
Shark | 0.00% | -0.08% | 0.03% | 0.00% | 0.02% | 0.07% | 100.7% | 98.9% | 99.8%
1024x768 | 0.00% | -0.03% | 0.00% | 0.00% | 0.01% | 0.03% | 99.3% | 100.4% | 99.9%
1920x1088 | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 0.07% | 100.4% | 99.4% | 99.9%
average | 0.00% | -0.01% | 0.00% | 0.00% | 0.01% | 0.05% | 100.0% | 99.8% | 99.9%
Notes: <number>

## Slide 9: Simulation results: Case 3
Case 3: Immediate (1/256, 1/256)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.07% | -0.02% | 0.00% | 0.02% | 0.15% | 101.3% | 98.8% | 99.6%
Kendo | 0.00% | -0.11% | 0.03% | 0.00% | 0.04% | 0.11% | 100.2% | 99.0% | 99.7%
Newspaper_CC | 0.00% | -0.04% | -0.01% | -0.01% | 0.01% | -0.03% | 100.1% | 99.4% | 99.9%
GT_Fly | 0.00% | -0.02% | -0.07% | -0.01% | 0.01% | 0.02% | 99.4% | 100.2% | 100.3%
Poznan_Hall2 | 0.00% | 0.10% | 0.02% | 0.01% | 0.02% | 0.11% | 100.2% | 99.4% | 99.9%
Poznan_Street | 0.00% | 0.01% | -0.02% | 0.00% | 0.03% | 0.05% | 99.3% | 98.5% | 99.6%
Undo_Dancer | 0.00% | -0.01% | 0.02% | 0.00% | 0.04% | 0.12% | 99.4% | 100.1% | 100.5%
Shark | 0.00% | -0.08% | 0.03% | 0.00% | 0.04% | 0.11% | 99.6% | 101.0% | 99.8%
1024x768 | 0.00% | -0.03% | 0.00% | 0.00% | 0.02% | 0.08% | 100.5% | 99.1% | 99.7%
1920x1088 | 0.00% | 0.00% | 0.00% | 0.00% | 0.03% | 0.08% | 99.6% | 99.8% | 100.0%
average | 0.00% | -0.01% | 0.00% | 0.00% | 0.03% | 0.08% | 100.0% | 99.5% | 99.9%
Notes: <number>

## Slide 10: Simulation results: Case 4
Case 4: Progressive (1/256, 1/1024)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.08% | -0.02% | 0.01% | 0.05% | 0.17% | 101.3% | 100.0% | 99.8%
Kendo | 0.00% | -0.11% | 0.04% | 0.00% | 0.06% | 0.18% | 100.3% | 99.8% | 100.1%
Newspaper_CC | 0.00% | -0.03% | -0.01% | -0.01% | 0.03% | -0.01% | 99.8% | 100.1% | 99.9%
GT_Fly | 0.00% | 0.12% | -0.11% | 0.00% | 0.03% | 0.08% | 98.5% | 100.7% | 100.4%
Poznan_Hall2 | 0.00% | 0.03% | 0.05% | 0.00% | 0.02% | 0.15% | 100.2% | 100.5% | 99.8%
Poznan_Street | 0.00% | 0.00% | -0.01% | -0.01% | 0.02% | 0.05% | 101.2% | 100.2% | 100.7%
Undo_Dancer | 0.00% | 0.06% | -0.04% | 0.01% | 0.06% | 0.17% | 99.7% | 100.5% | 99.8%
Shark | 0.00% | 0.00% | 0.05% | 0.01% | 0.06% | 0.17% | 100.7% | 99.3% | 100.0%
1024x768 | 0.00% | -0.02% | 0.00% | 0.00% | 0.04% | 0.11% | 100.5% | 100.0% | 99.9%
1920x1088 | 0.00% | 0.04% | -0.01% | 0.00% | 0.04% | 0.12% | 100.1% | 100.2% | 100.2%
average | 0.00% | 0.02% | -0.01% | 0.00% | 0.04% | 0.12% | 100.2% | 100.1% | 100.1%
Notes: <number>

## Slide 11: Simulation results: Case 5
Case 5: Immediate (1/1024, 1/1024)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.08% | -0.02% | 0.01% | 0.09% | 0.24% | 100.3% | 99.5% | 99.5%
Kendo | 0.00% | -0.11% | 0.04% | 0.00% | 0.07% | 0.20% | 100.5% | 100.2% | 100.2%
Newspaper_CC | 0.00% | -0.03% | -0.01% | -0.01% | 0.05% | 0.07% | 99.2% | 99.3% | 100.0%
GT_Fly | 0.00% | 0.12% | -0.11% | 0.00% | 0.03% | 0.13% | 101.3% | 99.7% | 99.9%
Poznan_Hall2 | 0.00% | 0.03% | 0.05% | 0.00% | 0.02% | 0.14% | 100.9% | 100.9% | 100.5%
Poznan_Street | 0.00% | 0.00% | -0.01% | -0.01% | 0.01% | 0.07% | 100.3% | 99.8% | 99.6%
Undo_Dancer | 0.00% | 0.06% | -0.04% | 0.01% | 0.08% | 0.20% | 100.8% | 101.2% | 100.2%
Shark | 0.00% | 0.00% | 0.05% | 0.01% | 0.08% | 0.25% | 100.8% | 99.7% | 99.8%
1024x768 | 0.00% | -0.02% | 0.00% | 0.00% | 0.07% | 0.17% | 100.0% | 99.7% | 99.9%
1920x1088 | 0.00% | 0.04% | -0.01% | 0.00% | 0.05% | 0.15% | 100.8% | 100.3% | 100.0%
average | 0.00% | 0.02% | -0.01% | 0.00% | 0.06% | 0.16% | 100.5% | 100.0% | 100.0%
Notes: <number>