## Slide 1: JCT3V-J0063: Cshift in HTM
Takanori Senoh, Koki Wakunami, Yasuyuki Ichihashi, Hisayuki Sasaki, Ryutaro Oi, Kenji Yamamoto

## Slide 2: Introduction
FTV AHG is expecting HTM, DERS and VSRS as the fundamental technologies for the development of future FTV standard.
However, a camera parameter, specifically Cshift for HTM has no inter-operability with the principal point X for DERS or VSRS.

## Slide 3: Cshift in HTM
HTM requires increasing Cshift (principal point X) when Position (translation X) decreases.
increase
decrease

## Slide 4: Principal point X in DERS/VSRS
DERS and VSRS require decreasing principal point X when translation X decreases.
Translation X
Principal point X
decrease
decrease

## Slide 5: Cshift in HTM
X
Z
0
Position
-3.711246
+3.711246
CShift
x
#View Num (cam ID)
101
102
100
x
x
960
969.86199
950.113801
Target
Principal Point
Origin of principal point x
That means Cshift (camera lens center) seems measured from the right side of image sensor. This seems unnatural.

## Slide 6: Principal point X in DERS/VSRS
X
Z
0
translation X
-3.711246
+3.711246
principal point x
x
#View Num (cam ID)
101
102
100
x
x
960
969.86199
950.113801
Target
Principal Point
Origin of principal point x
On the contrary, principal point X (camera lens center) is measured from the left side of image sensor in DERS and VSRS. This is natural.

## Slide 7: Recommendation
It is recommended HTM software is improved to be inter-operable with DERS and VSRS in terms of the camera parameter, specifically CShift since it is expected these software are fundamental technologies for the future FTV standard.