## Slide 1: Alignment of TMVP derivation process between 3D-HEVC and HEVC
Sejong University
Jae Yung Lee
Jong Ki Han
11th meeting: Geneva, CH
12~18 Feb. 2015

## Slide 2: Contents
Introduction
Problems
Proposed method
A bug-fix issue
Conclusions
Notes: 2

## Slide 3: Introduction[1/3]
Inter-view reference pictures are marked as ‘long-term reference picture’
ViewID based scaling process is adopted in 3D-HEVC

## Slide 4: Introduction[2/3]
Conditions of the scaled MV derivation process in merge mode
The TMVP derivation process of the current 3D-HEVC doesn’t discriminate between the inter-view prediction and the temporal long-term prediction.
IvMvScalingFlag | Current block | Collocated block | Derived TMVP
0 | short-term reference picture | short-term reference picture | Scaled TMVP based on POC
 | Each reference picture has different markings from another |  | Disabling TMVP
 | long-term reference picture | long-term reference picture | Scaled TMVP based on POC
1 | short-term reference picture | short-term reference picture | Scaled TMVP based on POC
 | Each reference picture has different markings from another |  | Disabling TMVP
 | long-term reference picture | long-term reference picture | Scaled TMVP based on ViewID

## Slide 5: Introduction[3/3]

## Slide 6: Problems[1/4]
Case 1: IvMvScalingFlag = 1
  The current block is predicted by inter-view reference picture.
  Denominator of scale factor is equal to ‘0’ when the collocated block is predicted by temporal long term reference picture.

## Slide 7: Problems[2/4]
currIvFlag = 1
colIvFlag = 1
colDiff = 0
currDiff = 1

## Slide 8: Problems[3/4]
Case 2: IvMvScalingFlag = 0
  The current block is predicted by temporal long term reference picture.
  Denominator of scale factor is equal to ‘0’ when the collocated block is predicted by inter-view reference picture.

## Slide 9: Problems[4/4]
currIvFlag = 1
colIvFlag = 1
colDiff = 0
currDiff = N

## Slide 10: Proposed method[1/3]
Alignment of TMVP derivation process between 3D-HEVC and HEVC
  When IvMvScalingFlag = 1
IvMvScalingFlag = 1 |  | 
Current block | Collocated block | Derived TMVP
Inter-view reference picture | Inter-view reference picture | Scaled TMVP based on ViewID
Non Inter-view reference picture | Inter-view reference picture | Disabling TMVP
Inter-view reference picture | Non Inter-view reference picture | Disabling TMVP
Non Inter-view reference picture | Non Inter-view reference picture | Derive TMVP as HEVC v.1 does

## Slide 11: Proposed method[2/3]
  When IvMvScalingFlag = 0
  The proposed method checks the difference between View IDs to specify the referencing type (among the inter-view prediction and temporal prediction) for the current and collocated blocks.
IvMvScalingFlag = 0 |  | 
Current block | Collocated block | Derived TMVP
Inter-view reference picture | Inter-view reference picture | No scaling
Non Inter-view reference picture | Inter-view reference picture | Disabling TMVP
Inter-view reference picture | Non Inter-view reference picture | Disabling TMVP
Non Inter-view reference picture | Non Inter-view reference picture | Derive TMVP as HEVC v.1 does

## Slide 12: Proposed method[3/3]

## Slide 13: Bug-fix in AltRefIdx [1/2]
Bug is in the process using AltRefIdx
The reference index of the current block should be initialized with 0, before considering MV of the center block.
However, in the current version of reference software, CurRefIdx is not initialized.
TMVP derivation process
in merge mode
(MV of ‘Right-bottom’ position
is checked using AltRefIdx)
availableFlagLXCol == 1?
(MV of ‘Center’ position
is checked using AltRefIdx)
availableFlagLXCol == 1?
mvLXcol = derived MV
mvLXcol = derived MV
mvLXcol is not available
Y
N
N
Y
mvLXcol = derived MV
Initialize a reference index
of current block
Initialize a reference index
of current block

## Slide 14: Bug-fix in AltRefIdx [2/2]
Solution
This contribution fixes the bug by adding the 2nd initialization just before considering the MV of the center block.
mvLXcol = derived MV
Initialize a reference index
of current block
Y
N
Initialize a reference index
of current block
TMVP derivation process
in merge mode
(MV of ‘Right-bottom’ position
is checked using AltRefIdx)
availableFlagLXCol == 1?
(MV of ‘Center’ position
is checked using AltRefIdx)
availableFlagLXCol == 1?
mvLXcol = derived MV
mvLXcol is not available
N
Y

## Slide 15: Conclusions
We can solve the problem of TMVP by discrimination between inter-view prediction and long-term prediction.
We suggest to fix a bug in the process using the Alternative Reference Index, AltRefIdx.
We appreciate Samsung and Sharp for their cross-checks. (JCT3V-K0062, JCT3V-K0059)

## Slide 16
Thank you!!