## Slide 1
Presenter : Jar-Ferr Yang
Center for Tomorrow Ubiquitous Cloud and Hypermedia Services
Institute of Computer and Communication Engineering
Department of Electrical Engineering
National Cheng Kung University
Centralized Texture-Depth Packing (CTDP) SEI Message

## Slide 2: Contents
Frame Compatible Centralized Texture‐Depth Packing (CTDP)
Centralized Texture-Depth Packing (CTDP) SEI Message Syntax
Experimental Results
Conclusions

## Slide 3: Frame Compatible Centrailzed Texture-Depth Packing (CTDP)

## Slide 4: Outlooks of CTDP Types (LR, TB)
CTDP-TB:
CTDP-LR:
H
H
W
W
WRD
WRD
W-WRD*2
H-HRD*2
HRD
HRD
H
W
depth_sampling_factor = 1, HRD=(H/48)*2
depth_sampling_factor = 2, HRD=(H/24)*2
depth_sampling_factor = 3, HRD=(H/16)*2
depth_sampling_factor = 1, WRD=(W/48)*2
depth_sampling_factor = 2, WRD=(W/24)*2
depth_sampling_factor = 3, WRD=(W/16)*2
Viewable for current 2D displays!

## Slide 5: Outlooks of CTDPs (2TB, 2LR)
H
H
W
W
H
H
W
CTDP-2TB:
W
depth_sampling_factor = 1, HRD =(H/48)*2
depth_sampling_factor = 2, HRD =(H/24)*2
depth_sampling_factor = 3, HRD =(H/16)*2
H-HRD*2
HRD
HRD
CTDP-LR:
WRD
WRD
W-WRD*2
H
depth_sampling_factor = 1, WRD=(W/48)*2
depth_sampling_factor = 2, WRD=(W/24)*2
depth_sampling_factor = 3, WRD=(W/16)*2
Viewable for current SbS and TaB 3D displays!

## Slide 6
1600
160
160
1088
1920
908
90
90
Example 1 (5/6):
1920x1088
1088/24=45.3333
[H/24]*2=90
H-[H/24]*4=908
1920/24=80
[W/24]*2=160
W-[W/24]*4=1600
True Texture ratio = 908/1088
True Depth ratio=540/1088
True Texture ratio = 1600/1920=5/6
True Depth ratio=640/1920=3/6
Notes: =5/6

## Slide 7
1600
160
160
1080
1920
900
90
90
Example 2 (5/6):
1920x1080
1080/24=45
[H/24]*2=90
H-[H/24]*4=900
1920/24=80
[W/24]*2=160
W-[W/24]*4=1600
True Texture ratio = 1600/1920=5/6
True Depth ratio=640/1920=3/6
True Texture ratio = 900 /1920= 5/6
True Depth ratio=960/1920=3/6

## Slide 8
640
64
64
768
1024
856
84
84
Example 3 (5/6):
1024x768
768/24=32
[H/24]*2=64
H-[H/24]*4=640
1024/24=42.666
[W/24]*2=84
W-[W/24]*4=856
True Texture ratio = 640 /768= 5/6
True Depth ratio=384/768=3/6
True Texture ratio = 856/1024
True Depth ratio=504/1024

## Slide 9: CTDP-TB Packing Procedure
Vertical Splitting
& Flipping
Downscaling in
Vertical Direction
Downscaling in
Vertical Direction
YCbCr Color Format Conversion
Combination
H
H
H
Pixels Rearrangement to RGB Subpixels Channel
Pixel Rearrangement to
RGB Subpixels Channel
HRD
H- HRD*2
H- HRD*2
HRD
HRD
HRD
HRD*2
HRD*6
R
G
B
depth_sampling_factor = 1, HRD =(H/48)*2
depth_sampling_factor = 2, HRD =(H/24)*2
depth_sampling_factor = 3, HRD =(H/16)*2
w
w
w
w
w
w

## Slide 10: CTDP-TB Depacking Procedure
H
= (
depth_sampling_factor = 1, HRD =(H/48)*2
depth_sampling_factor = 2, HRD =(H/24)*2
depth_sampling_factor = 3, HRD =(H/16)*2
H- HRD*2
HRD
HRD
Upscaling in
Vertical Direction
H
H
View and Depth Splitting
Inverse YCbCr Color Format Conversion
Vertical Flipping & Combination
Get Depth Pixel from
RGB Subpixels Channel
Upscaling in
Vertical Direction
Depth Enhancement
(Optional)
H- HRD*2
HRD
HRD
HRD*2
HRD*6
W
W

## Slide 11: CTDP-LR Packing Procedure
Horizontal Splitting
& Flipping
Downscaling in
Horizontal Direction
Downscaling in
Horizontal Direction
YCbCr Color Format Conversion
Combination
W
W
Pixel Rearrangement to
RGB Subpixels Channel
WRD*2
WRD
W-WRD*2
WRD
W-WRD*2
WRD
WRD
WRD*6
1 2 3 4 5 6 7 8 9
1 2 3
Depth
R
G
B
Pixels Rearrangement to YCbCr Subpixels Channel
depth_sampling_factor = 1, WRD=(W/48)*2
depth_sampling_factor = 2, WRD=(W/24)*2
depth_sampling_factor = 3, WRD=(W/16)*2
H
H
H
H
H
H
H

## Slide 12: CTDP-LR Depacking Procedure
Upscaling in
Horizontal Direction
View and Depth Splitting
Inverse YCbCr Color Format Conversion
Horizontal Flipping & Combination
Get Depth Pixel from
RGB Subpixels Channel
Upscaling in
Horizontal Direction
Depth Enhancement
(Optional)
W
W
WRD*2
W-WRD*2
WRD
WRD
W-WRD*2
WRD*6
= (
depth_sampling_factor = 1, WRD=(W/48)*2
depth_sampling_factor = 2, WRD=(W/24)*2
depth_sampling_factor = 3, WRD=(W/16)*2
WRD
WRD
H
H
H
H
H
H
H

## Slide 13: CTDP-2TB Packing Procedure
H
Pixels Rearrangement to RGB Subpixels Channel
W
W
W
W
H
Combination & Downscaling in Horizontal Direction by 2
Combination & Downscaling in Horizontal Direction by 2
W
H
W
W
W
W
W
W
H
H- HRD*2
HRD
HRD
H- HRD *2
Vertical Splitting
& Flipping
Downscaling in
Vertical Direction
Downscaling in
Vertical Direction
YCbCr Color Format Conversion
Combination
Pixel Rearrangement to
RGB Subpixels Channel
depth_sampling_factor = 1, HRD=(H/48)*2
depth_sampling_factor = 2, HRD=(H/24)*2
depth_sampling_factor = 3, HRD=(H/16)*2
R
G
B
HRD
HRD
HRD*2
HRD*6

## Slide 14: CTDP-2TB Depacking Procedure
Upscaling in
Vertical Direction
View and Depth Splitting
Inverse YCbCr Color Format Conversion
Vertical Flipping & Combination
Get Depth Pixel from
RGB Subpixels Channel
Upscaling in
Vertical Direction
Depth Enhancement
(Optional)
Splitting & Upscaling in
Horizontal by 2
Splitting & Upscaling in
Horizontal by 2
W
H
W
H
W
W
W
W
H
W
H
W
HRD
HRD
H-HRD*2
H-HRD*2
W
W
HRD
HRD
HRD*2
HRD*6
= (
depth_sampling_factor = 1, HRD=(H/48)*2
depth_sampling_factor = 2, HRD=(H/24)*2
depth_sampling_factor = 3, HRD=(H/16)*2

## Slide 15: CTDP-2LR Packing Procedure
Vertical Splitting
& Flipping
Downscaling in
Vertical Direction
Downscaling in
Vertical Direction
YCbCr Color Format Conversion
Combination
H
W
W
W
W
H
Combination & Downscaling in Horizontal Direction by 2
Combination & Downscaling in Horizontal Direction by 2
W
H
W
H
H
H
H
H
H
W- WRD*2
WRD*2
WRD*6
Pixel Rearrangement to
RGB Subpixels Channel
WRD
WRD
W- WRD*2
1 2 3
1 2 3 4 5 6 7 8 9
Depth
R
G
B
Pixels Rearrangement to YCbCr Subpixels Channel
depth_sampling_factor = 1, WRD=(W/48)*2
depth_sampling_factor = 2, WRD=(W/24)*2
depth_sampling_factor = 3, WRD=(W/16)*2
WRD
WRD
H

## Slide 16: CTDP-2LR Depacking Procedure
Upscaling in
Horizontal Direction
Splitting & Upscaling in
Vertical by 2
H
W
W
H
= (
H
WRD*6
H
W
H
W
H
W- WRD*2
H
WRD
WRD
H
WRD*2
H
WRD
WRD
View and Depth Splitting
Inverse YCbCr Color Format Conversion
Vertical Flipping & Combination
Get Depth Pixel from
RGB Subpixels Channel
Upscaling in
Horizontal Direction
Depth Enhancement
(Optional)
Splitting & Upscaling in
Vertical by 2
W
W
W- WRD*2
depth_sampling_factor = 1, FaW =(W/48)*2
depth_sampling_factor = 2, FaW =(W/24)*2
depth_sampling_factor = 3, FaW =(W/16)*2

## Slide 17: Centralized Texture-Depth Packing (CTDP) SEI Message Syntax

## Slide 18: CTDP SEI Syntax
centralized_texture-depth_packing( payloadSize ) { | Descriptor
centralized_texture-depth_packing_cancel_flag | u(1)
if( ! centralized_texture-depth_packing_cancel_flag) { | 
depth_sampling_factor | u(3)
centralized_texture-depth_packing_content_interpretation_type | u(3)
depth_spatial_flipping_flag | u(1)
depth_subpixel_arrangement_type | u(2)
texture_samping_type | u(3)
depth_samping_type | u(3)
depth_chroma_sampling_type | u(3)
centralized_texture-depth_packing_persistence_flag | u(1)
} | 
} | 

## Slide 19: depth_sampling_factor
Value | Interpretation
0 | Unspecified the downscale method between the centralized texture-depth packed constituent frames.
1 | Each depth frame in centralized texture-depth packing arrangement represents about 4:1 decimation from the original depth frame horizontally or vertically and about 12:11 decimation from the original texture frame horizontally or vertically, starting from the top or left-most sample.
2 | Each depth frame in centralized texture-depth packing arrangement represents about 4:2 decimation from the original depth frame horizontally or vertically and about 12:10 decimation from the original texture frame horizontally or vertically, starting from the top or left-most sample.
3 | Each depth frame in centralized texture-depth packing arrangement represents about 4:3 decimation from the original depth frame horizontally or vertically and about 12:9 decimation from the original texture frame horizontally or vertically, starting from the top or left-most sample.

## Slide 20: centralized_texture-depth_packing_content_interpretation_type
Value | Interpretation
0 | Indicates that the packed frame is arranged in order of reduced_depth_top (RDT), resized_texture (RT), and reduced_depth_bottom (RDB) from top to bottom called as CTDP TB type as illustrated in Figure D‑X1.
1 | Indicates that the packed frame is arranged in order of reduced_depth_left (RDL), resized_texture (RT), and reduced_depth_right (RDR) from left to right called as CTDP LR type as illustrated in Figure D‑X2.
2 | Indicates that the packed frame, which provides two texture-plus-depth views, is arranged in order of reduced_depth_leftview_top (RDLT), reduced_depth_rightview_top (RDRT), resized_texture_leftview (RTL), resized_texture_rightview (RTR), reduced_depth_leftview_bottom (RDLB), and reduced_depth_rightview_bottom (RDRB),, from upper left, upper right to lower right called as CTDP 2TB type as illustrated in Figure D‑X3.
3 | Indicates that the packed frame, which provides two texture-plus-depth views, is arranged in order of reduced_depth_topview_left (RDTL), reduced_depth_bottomview_left (RDBL), resized_texture_topview (RTT), resized_texture_bottomview (RTB), reduced_depth_topview_right (RDTR) and reduced_depth_bottomview_right (RDBR) from upper left, upper center to lower right called as CTDP 2LR type as illustrated in Figure D‑X4.
CTDP-TB
CTDP-LR
CTDP-2TB
CTDP-2LR

## Slide 21: texture_samping_type
texture_samping_type indicates that the method of the texture sampling is used by an encoder to indicate to a decoder as specified in Table DX‑3.
Value | Interpretation
1 | Encoder using bilinear method to downscale the vertical or horizontal resolution of texture frame
2 | Encoder using bicubic method to downscale the vertical or horizontal resolution of texture frame

## Slide 22: depth_samping_type
depth_samping_type indicates that the method of the depth sampling is used by an encoder to indicate to a decoder as specified in Table DX‑4.
Value | Interpretation
1 | Encoder using bilinear method to downscale the vertical or horizontal resolution of depth frame
2 | Encoder using bicubic method to downscale the vertical or horizontal resolution of depth frame

## Slide 23
Depth-chroma_sampling_type indicates that the depth chroma sampling method from 444 to 422 or 420 format is used by an encoder to indicate to a decoder as specified in Table D-X5.
Depth_chroma_sampling_type
Value | Interpretation
1 | Encoder using the direct sample to convert the chroma sample from 444 to 422 or 420 format according to marked chroma sample location.
2 | Encoder using the mean of two (four) samples to convert the chroma sample from 444 to 422 (420) format.

## Slide 24: Experimental Results
Environment Settings
Coding performance in HEVC HM 13.0 (CTDP)
Coding performance in 3D-HEVC HTM 8.0

## Slide 25: Test Sequences (Nature)
No. | Sequence | Size | Frames | Fps
S01 | Poznan Hall | 1920*1088 | 200 | 25
S06 | Balloons | 1024*768 | 300 | 30

## Slide 26: Experimental Settings
Encoding Mode: All Intra, Low delay, Random access
QP: 27,32,37,42
depth_sampling_factor: 3/4, 5/6, 11/12
CTDP_content_interpretation_type:
CTDP-LR, CTDP-TB, CTDP-2LR, CTDP-2TB
image resizing: bicubic
  depth resizing: bicubic
  depth spatial flipping: flipped
  depth subpixel arrangement: sequential order
  depth_chorma_sampling: direct sample

## Slide 27: Case 1 - 2D View & Depth Reconstruction
HEVC Codec
Packing
De-packing
Depth
Texture
Bit Rate
PSNR
PSNR Calculation
3D HEVC
Codec

## Slide 28
HEVC Coding
Packing
De-packing
Depth
Texture
Bit Rate
PSNR
PSNR Calculation
Case 2-3D
Target View Reconstruction
DIBR
Original
Vertical (3/4)
Vertical (7/8)
Vertical (15/16)
DIBR
3D HEVC
Codec

## Slide 29: Coding Performance Comparison (HM v13.0)

## Slide 30: Experimental Results (1V1D) HEVC+CTDP-TB with respect to 3D-HEVC
BDBR |  |  |  |  |  |  |  |  | 
 | Case 1 (without DIBR) % |  |  |  |  |  | Case 2 (DIBR) % |  | 
 | Texture |  |  | Depth |  |  | Texture |  | 
 | 3/4_TB | 5/6_TB | 11/12_TB | 3/4_TB | 5/6_TB | 11/12_TB | 3/4_TB | 5/6_TB | 11/12_TB
ra | 6.2239 | 4.4280 | 1.6398 | -66.0864 | -48.1555 | -11.1862 | 20.6479 | 29.6362 | 51.7023
ldp | 5.8982 | 2.5706 | -1.1583 | -74.0706 | -63.4232 | -38.2969 | 13.2991 | 21.8319 | 37.6035
ai | 0.5457 | 0.3540 | -0.7842 | -47.5548 | -25.7799 | 14.7971 | 16.4881 | 28.3499 | 52.0140
ave | 4.2226 | 2.4509 | -0.1009 | -62.5706 | -45.7862 | -11.5620 | 16.8117 | 26.6060 | 47.1066
BDPSNR |  |  |  |  |  |  |  |  | 
 | Case 1 (without DIBR) dB |  |  |  |  |  | Case 2 (DIBR) dB |  | 
 | Texture |  |  | Depth |  |  | Texture |  | 
 | 3/4_TB | 5/6_TB | 11/12_TB | 3/4_TB | 5/6_TB | 11/12_TB | 3/4_TB | 5/6_TB | 11/12_TB
ra | -0.2692 | -0.1897 | -0.0793 | 3.9972 | 2.4871 | 0.5060 | -0.5537 | -0.7519 | -1.2206
ldp | -0.2943 | -0.1695 | -0.0256 | 5.9015 | 4.4044 | 2.1536 | -0.4006 | -0.5940 | -0.9875
ai | -0.0582 | -0.0270 | 0.0253 | 3.8979 | 1.7430 | -0.8352 | -0.5731 | -0.8944 | -1.5320
ave | -0.2072 | -0.1287 | -0.0265 | 4.5989 | 2.8781 | 0.6081 | -0.5091 | -0.7468 | -1.2467

## Slide 31: RD Curves-RA
HEVC+CTDP-TB versus 3D-HEVC (1V1D)
Texture Y
Depth Y
DIBR Texture Y

## Slide 32: RD Curves-LDP
HEVC+CTDP-TB versus 3D-HEVC (1V1D)
Texture Y
Depth Y
DIBR Texture Y

## Slide 33: RD Curves-AI
HEVC+CTDP-TB versus 3D-HEVC (1V1D)
Texture Y
Depth Y
DIBR Texture Y

## Slide 34
Decoded and View Synthesis frame comparison

## Slide 35: Decoded and View Synthesis frame - LDP
Texture Y
Depth Y
DIBR Texture Y
3D
HTM
3/4
CTDP
HEVC+CTDP-TB versus 3D-HEVC (1V1D , QP=42)

## Slide 36
Decoded and View Synthesis frame comparison

## Slide 37: Decoded and View Synthesis frame - LDP
Texture Y
Depth Y
DIBR Texture Y
3D
HTM
3/4
CTDP
HEVC+CTDP-TB versus 3D-HEVC (1V1D , QP=42)

## Slide 38: Experimental Results (1V1D) HEVC+CTDP-LR with respect to 3D-HEVC
BDBR |  |  |  |  |  |  |  |  | 
 | Case 1 (without DIBR) % |  |  |  |  |  | Case 2 (DIBR) % |  | 
 | Texture |  |  | Depth |  |  | Texture |  | 
 | 3/4_LR | 5/6_LR | 11/12_LR | 3/4_LR | 5/6_LR | 11/12_LR | 3/4_LR | 5/6_LR | 11/12_LR
ra | 12.5590 | 8.9520 | 5.8570 | -57.7360 | -37.8310 | 19.6350 | 38.8420 | 52.5130 | 106.7110
ldp | 13.1730 | 8.6210 | 4.7550 | -67.5150 | -53.9830 | -20.9340 | 30.6720 | 43.3780 | 82.9880
ai | 2.5300 | 0.8960 | -0.6790 | -39.6840 | -17.1490 | 29.7290 | 29.5840 | 45.7330 | 93.3510
ave | 9.4210 | 6.1570 | 3.3110 | -54.9790 | -36.3210 | 9.4770 | 33.0330 | 47.2080 | 94.3500
BDPSNR |  |  |  |  |  |  |  |  | 
 | Case 1 (without DIBR) dB |  |  |  |  |  | Case 2 (DIBR) dB |  | 
 | Texture |  |  | Depth |  |  | Texture |  | 
 | 3/4_LR | 5/6_LR | 11/12_LR | 3/4_LR | 5/6_LR | 11/12_LR | 3/4_LR | 5/6_LR | 11/12_LR
ra | -0.4450 | -0.3410 | -0.2430 | 3.0400 | 1.6950 | -0.6530 | -0.9560 | -1.2520 | -2.1200
ldp | -0.5120 | -0.3740 | -0.2480 | 4.8060 | 3.3780 | 0.9430 | -0.8240 | -1.1010 | -1.8560
ai | -0.1290 | -0.0770 | -0.0100 | 2.7700 | 0.9640 | -1.8050 | -0.9320 | -1.3760 | -2.3680
ave | -0.3620 | -0.2640 | -0.1670 | 3.5390 | 2.0120 | -0.5050 | -0.9040 | -1.2430 | -2.1150

## Slide 39: RD Curves-RA
HEVC+CTDP-LR versus 3D-HEVC (1V1D)
Texture Y
Depth Y
DIBR Texture Y

## Slide 40: RD Curves-LDP
HEVC+CTDP-LR versus 3D-HEV (1V1D)
Texture Y
Depth Y
DIBR Texture Y

## Slide 41: RD Curves-AI
HEVC+CTDP-LR versus 3D-HEVC (1V1D)
Texture Y
Depth Y
DIBR Texture Y

## Slide 42
Decoded and View Synthesis frame comparison

## Slide 43: Decoded and View Synthesis frame - LDP
Texture Y
Depth Y
DIBR Texture Y
3D
HTM
3/4
CTDP
HEVC+CTDP-LR vs 3D-HEVC (1V1D, QP=42)

## Slide 44
Decoded and View Synthesis frame comparison

## Slide 45: Decoded and View Synthesis frame - LDP
Texture Y
Depth Y
DIBR Texture Y
3D
HTM
3/4
CTDP
HEVC+CTDP-LR vs 3D-HEVC (1V1D, QP=42)

## Slide 46: Experimental Results HEVC+CTDP-2TB with respect to 3D-HEVC 2V2D
BDBR |  |  |  |  |  |  |  |  | 
 | Case 1 (without DIBR) % |  |  |  |  |  | Case 2 (DIBR) % |  | 
 | Texture |  |  | Depth |  |  | Texture |  | 
 | 3/4_TB | 5/6_TB | 11/12_TB | 3/4_TB | 5/6_TB | 11/12_TB | 3/4_TB | 5/6_TB | 11/12_TB
ra | 49.6972 | 49.3408 | 47.8346 | -64.2652 | -46.0313 | -7.165 | 31.4132 | 37.3969 | 45.7124
ldp | 30.5254 | 29.4065 | 27.9917 | -72.7051 | -59.5775 | -30.8238 | 18.7458 | 23.3038 | 30.5326
ai | -24.0089 | -23.6773 | -24.2281 | -60.5032 | -45.3891 | -18.386 | -17.3841 | -11.8381 | -4.3706
ave | 18.7379 | 18.3567 | 17.1994 | -65.8245 | -50.3326 | -18.7916 | 10.925 | 16.2875 | 23.9581
BDPSNR |  |  |  |  |  |  |  |  | 
 | Case 1 (without DIBR) dB |  |  |  |  |  | Case 2 (DIBR) dB |  | 
 | Texture |  |  | Depth |  |  | Texture |  | 
 | 3/4_TB | 5/6_TB | 11/12_TB | 3/4_TB | 5/6_TB | 11/12_TB | 3/4_TB | 5/6_TB | 11/12_TB
ra | -1.4741 | -1.4598 | -1.4186 | 3.6716 | 2.2621 | 0.3656 | -1.0424 | -1.1807 | -1.3672
ldp | -1.0797 | -1.0294 | -0.9726 | 5.0202 | 3.5139 | 1.4437 | -0.7550 | -0.8793 | -1.0728
ai | 1.1860 | 1.1778 | 1.2229 | 5.4209 | 3.3579 | 0.8754 | 0.7630 | 0.4521 | 0.0511
ave | -0.4559 | -0.4372 | -0.3895 | 4.7042 | 3.0446 | 0.8949 | -0.3448 | -0.5360 | -0.7963

## Slide 47: RD Curves-RA
HEVC+CTDP-2LR versus 3D-HEVC 2V2D
Texture Y
Depth Y
DIBR Texture Y

## Slide 48: RD Curves-LDP
HEVC+CTDP-2LR versus 3D-HEVC 2V2D
Texture Y
Depth Y
DIBR Texture Y

## Slide 49: RD Curves-AI
HEVC+CTDP-2LR versus 3D-HEVC 2V2D
Texture Y
Depth Y
DIBR Texture Y

## Slide 50
Decoded and View Synthesis frame comparison

## Slide 51: Decoded and View Synthesis frame - LDP
Texture Y
Depth Y
DIBR Texture Y
3D
HTM
3/4
CTDP
HEVC+CTDP-2LR vs 3D-HEVC (2V2D, QP=37)

## Slide 52
Decoded and View Synthesis frame comparison

## Slide 53: Decoded and View Synthesis frame - LDP
Texture Y
Depth Y
DIBR Texture Y
3D
HTM
3/4
CTDP
HEVC+CTDP-2LR vs 3D-HEVC (2V2D, QP=37)

## Slide 54: Conclusions
This contribution proposes modified CTDP SEI Message which is an update of the prior contribution JCT3V-J0108, by adding two-view plus two-depth types in centralized texture-depth packing content interpretation type. This contribution also limits the frame size of reduced depth regions to be even
The objective measurements of the proposed texture-3/4, texture-5/6 and texture-11/12 CTDP formats with LR, TB, 2LR 2TB configurations are compared to those of the one-view plus one-depth and two-view plus two-depth coded by 3D-HEVC.
HEVC+CDTP formats show some advantage in low bit rate coding.
Once CTDP SEI Message is accepted by MPEG, ChungHwa Telecom MOD System and Hsin-Yeong An Cable TV Company will adopt it for their 3D video services.
China AVS2 has accepted the texture reduction ratio 5/6 for CTDP LR, TB, 2LR, and 2TB for future AVS2 baseline_3D_packing profile.

## Slide 55
Thanks for your kind attention
Q&A