## Slide 1
Redundant signaling removal in SPS 3D extension
February 2015
LG Electronics
Sunmi Yoo, Junghak Nam, Sehoon Yea

## Slide 2: Introduction
Redundant flag signaling in SPS 3D extension
  Recognizable whether the current SPS is texture or depth (from VPS)
  But currently transmitted twice for texture and depth
No need to send flags for both components (texture and depth) in SPS
  If current SPS is for texture, depth coding tool flags must be zero (and vice versa).
Proposed method
  To send flags according to its component
    Only texture 3D coding tool flag transmission for texture SPS
    Only depth 3D coding tool flag transmission for depth SPS

## Slide 3: Proposed method
Method 1 : Flag array method
  Each flag is stored for both texture and depth, with an array.
  E.g. iv_res_pred_flag[DepthFlag]
    Note that iv_res_pred_flag[DepthFlag==1] is always set to zero.
Method 2 : Single flag method
  Each flag is stored as one byte variable.
  E.g. iv_res_pred_flag
Second method is desirable
  Less memory allocation for coding tool flags in decoder
  Simple