## Slide 1
www.hisilicon.com
The Right silicon for your next BIG idea
Cleanup of Single Depth Intra Mode simplification
Jianhua Zheng, Zhouye Gu2
Xu Chen, Xiaozhen Zheng,
Yongbing Lin, Nam Ling2
Philipp Zhang
JCT3V-K0051
HiSilicon Technologies1 and Santa Clara University2

## Slide 2: Summary of Proposals
Thanks Sharp for cross-checking, JCT-3V K0061
  In JCT-3V 10th meeting held in Strasbourg, FR, for the single depth intra mode, it was agreed to reduce the candidate number from 5 to 2 and the remove the pruning process.
  reduce candidates from 5 to 2
  remove pruning
  In J0116 and J0065, it was proposed to further simply the single depth intra mode by removing the candidate list derivation procedure.
  In this contribution, the results of the further cleanup of single depth mode simplification based on HTM13.0 is reported,
  Further clean up on the candidate list derivation
The impact on the coding efficiency of single depth intra coding is negligible.
AI: 0.01%, CTC: 0.02%

## Slide 3: Problem
  Although the number of candidates is reduced to 2, a candidate list derivation procedure is still needed to derive the sample candidate to fill the current CU.
  The worse case of checking available status of the neighboring sample candidates is always as two time. After checking the available of the candidates, an offset is determined.
Figure 1 candidate positions (An/2, B n/2).
Since the number of candidates has been reduced to 2, the process to determine the final sample candidate can be simplified.

## Slide 4: Proposed Simplification
DepthVal is set to 128 (2bitDepth-1 when bitDepth=8)
Checking the availability of the reference pixel (An/2 or Bn/2) according to the singling of single_sample_idx.
If the reference pixel is available, DepthVal is equals to the available pixel, and DepthVal is selected to fill the current CU;
Method:
Benefits:
- The determination of the depth value to fill the current CU can be done without the candidate list derivation process.
- The worse case of the reference pixel availability checking is further reduced from two to one.
Figure 1 candidate positions (An/2, B n/2).

## Slide 5: Proposed Simplification

## Slide 6: Experimental results
Page 6
AI
CTC

## Slide 7: Spec. Changes

## Slide 8: Spec. Changes

## Slide 9: Conclusion
It was proposed
- remove candidate list derivation process in SDM mode,
- further simplify the reference pixel availability checking, reduced to
from 2 to 1
The experiments results show negligible coding efficiency impact.

## Slide 10
Thank you!
www.hisilicon.com