## Slide 1
Presenter : Jar-Ferr Yang
Center for Tomorrow Ubiquitous Cloud and Hypermedia Services
Institute of Computer and Communication Engineering
Department of Electrical Engineering
National Cheng Kung University, Taiwan
Revised Centralized Texture-Depth Packing SEI Message and Its Performance Improvement by Depth Enhancement
(Revisions of JCT3V-J0108 and JCT3V-k0027)

## Slide 2: Contents
Frame Compatible Centralized Texture‐Depth Packing (CTDP)
Centralized Texture-Depth Packing (CTDP) SEI Message Syntax
Depth Enhancement for CTDP Depacking
Experimental Results of Enhanced CTDP Depacking
CTDP Adoption Plans in Taiwan
Conclusions

## Slide 3: Frame Compatible Centrailzed Texture-Depth Packing (CTDP)
depth_sampling_factor = 1,
Texture resized to 11/12, Depth resized to 3/12,
depth_sampling_factor = 2,
Texture resized to 5/6, Depth resized to 3/6, depth_sampling_factor = 3,
Texture resized to 3/4, Depth resized to 3/4,
k = 2packed_depth_size_factor+1
To control half-color-packed depth size to be multiple of 2, 4, 8, or 16

## Slide 4: CTDP-TB Packing Procedure
Vertical Splitting
& Flipping
Downscaling in
Vertical Direction
Downscaling in
Vertical Direction
YCbCr Color Format Conversion
Combination
H
H
H
Pixels Rearrangement to RGB Subpixels Channel
Pixel Rearrangement to
RGB Subpixels Channel
HRD
H- HRD*2
H- HRD*2
HRD
HRD
HRD
HRD*2
HRD*6
R
G
B
depth_sampling_factor = 1, HRD =(H/24k)*k
depth_sampling_factor = 2, HRD =(H/12k)*k
depth_sampling_factor = 3, HRD =(H/8k)*k
w
w
w
w
w
w

## Slide 5: CTDP-LR Packing Procedure
Horizontal Splitting
& Flipping
Downscaling in
Horizontal Direction
Downscaling in
Horizontal Direction
YCbCr Color Format Conversion
Combination
W
W
Pixel Rearrangement to
RGB Subpixels Channel
WRD*2
WRD
W-WRD*2
WRD
W-WRD*2
WRD
WRD
WRD*6
1 2 3 4 5 6 7 8 9
1 2 3
Depth
R
G
B
Pixels Rearrangement to YCbCr Subpixels Channel
depth_sampling_factor = 1, WRD=(W/24k)*k
depth_sampling_factor = 2, WRD=(W/12k)*k
depth_sampling_factor = 3, WRD=(W/8k)*k
H
H
H
H
H
H
H

## Slide 6: Outlooks of CTDP Types (LR, TB)
CTDP-TB:
CTDP-LR:
H
H
W
W
WRD
WRD
W-WRD*2
H-HRD*2
HRD
HRD
H
W
Viewable for current 2D displays!
depth_sampling_factor = 1, HRD=(H/(24k))*k
depth_sampling_factor = 2, HRD=(H/(12k))*k
depth_sampling_factor = 3, HRD=(H/(8k))*k
depth_sampling_factor = 1, WRD=(W/(24k))*k
depth_sampling_factor = 2, WRD=(W/(12k))*k
depth_sampling_factor = 3, WRD=(W/(8k))*k
k = 2packed_depth_size_factor+1

## Slide 7
1600
160
160
1080
1920
900
90
90
Example 1: Texture-5/6,1920x1080
HRD=floor(H/24)*2=90
HRT = H-HRD*2=900
WRD=floor(W/24)*2=160
WRT = W-WRD*2=1600
True Texture ratio = 1600/1920=5/6
True Depth ratio=640/1920=3/6
True Texture ratio = 900 /1920= 5/6
True Depth ratio=960/1920=3/6
If packed_depth_size_factor = 0
K=2

## Slide 8
Example 2: Texture-5/6 CTDP-TB 1920x1088
k=2, HRD=floor(H/(12k))*k=90
HRT = H - HRD*2 = 908
packed_depth_size_factor = 0
(k=2)
1920
908
90
90
packed_depth_size_factor = 1 or 2
(k = 4 or 8)
1920
912
88
88
packed_depth_size_factor=3
(k = 16)
1920
928
80
80
k=4, HRD=floor(H/(12k))*k=88
HRT = H - HRD*2 = 912
k=16, HRD=floor(H/(12k))*k=80
HRT = H - HRD*2 = 928
Notes: =5/6

## Slide 9: CTDP-TB Depacking Procedure
H
= (
depth_sampling_factor = 1, HRD =(H/24k)*k
depth_sampling_factor = 2, HRD =(H/12k)*k
depth_sampling_factor = 3, HRD =(H/8k)*k
H- HRD*2
HRD
HRD
Upscaling in
Vertical Direction
H
H
View and Depth Splitting
Inverse YCbCr Color Format Conversion
Vertical Flipping & Combination
Get Depth Pixel from
RGB Subpixels Channel
Upscaling in
Vertical Direction
Depth Enhancement
(Optional)
H- HRD*2
HRD
HRD
HRD*2
HRD*6
W
W

## Slide 10: CTDP-LR Depacking Procedure
Upscaling in
Horizontal Direction
View and Depth Splitting
Inverse YCbCr Color Format Conversion
Horizontal Flipping & Combination
Get Depth Pixel from
RGB Subpixels Channel
Upscaling in
Horizontal Direction
Depth Enhancement
(Optional)
W
W
WRD*2
W-WRD*2
WRD
WRD
W-WRD*2
WRD*6
= (
depth_sampling_factor = 1, WRD=(W/24k)*k
depth_sampling_factor = 2, WRD=(W/12k)*k
depth_sampling_factor = 3, WRD=(W/8k)*k
WRD
WRD
H
H
H
H
H
H
H

## Slide 11: CTDP-2TB Packing Procedure
H
Pixels Rearrangement to RGB Subpixels Channel
W
W
W
W
H
Combination & Downscaling in Horizontal Direction by 2
Combination & Downscaling in Horizontal Direction by 2
W
H
W
W
W
W
W
W
H
H- HRD*2
HRD
HRD
H- HRD *2
Vertical Splitting
& Flipping
Downscaling in
Vertical Direction
Downscaling in
Vertical Direction
YCbCr Color Format Conversion
Combination
Pixel Rearrangement to
RGB Subpixels Channel
depth_sampling_factor=1, HRD=(H/24)*k
depth_sampling_factor=2, HRD=(H/12k)*k
depth_sampling_factor=3, HRD=(H/8k)*k
R
G
B
HRD
HRD
HRD*2
HRD*6

## Slide 12: CTDP-2LR Packing Procedure
Vertical Splitting
& Flipping
Downscaling in
Vertical Direction
Downscaling in
Vertical Direction
YCbCr Color Format Conversion
Combination
H
W
W
W
W
H
Combination & Downscaling in Horizontal Direction by 2
Combination & Downscaling in Horizontal Direction by 2
W
H
W
H
H
H
H
H
H
W- WRD*2
WRD*2
WRD*6
Pixel Rearrangement to
RGB Subpixels Channel
WRD
WRD
W- WRD*2
1 2 3
1 2 3 4 5 6 7 8 9
Depth
R
G
B
Pixels Rearrangement to YCbCr Subpixels Channel
depth_sampling_factor=1, WRD=(W/24k)*k
depth_sampling_factor=2, WRD=(W/12k)*k depth_sampling_factor=3, WRD=(W/8k)*k
WRD
WRD
H

## Slide 13: Outlooks of CTDPs (2TB, 2LR)
H
H
W
W
H
H
H-HRD*2
HRD
HRD
WRD
WRD
W-WRD*2
H
Viewable for current SbS and TaB 3D displays!
CTDP-TB:
CTDP-LR:
depth_sampling_factor = 1, HRD=(H/24k)*k
depth_sampling_factor = 2, HRD=(H/12k)*k
depth_sampling_factor = 3, HRD=(H/8k)*k
depth_sampling_factor = 1, WRD=(W/24k)*k
depth_sampling_factor = 2, WRD=(W/12k)*k
depth_sampling_factor = 3, WRD=(W/8k)*k
k = 2packed_depth_size_factor+1

## Slide 14: CTDP-2TB Depacking Procedure
Upscaling in
Vertical Direction
View and Depth Splitting
Inverse YCbCr Color Format Conversion
Vertical Flipping & Combination
Get Depth Pixel from
RGB Subpixels Channel
Upscaling in
Vertical Direction
Depth Enhancement
(Optional)
Splitting & Upscaling in
Horizontal by 2
Splitting & Upscaling in
Horizontal by 2
W
H
W
H
W
W
W
W
H
W
H
W
HRD
HRD
H-HRD*2
H-HRD*2
W
W
HRD
HRD
HRD*2
HRD*6
= (
depth_sampling_factor = 1, HRD=(H/24k)*k
depth_sampling_factor = 2, HRD=(H/12k)*k
depth_sampling_factor = 3, HRD=(H/8k)*k

## Slide 15: CTDP-2LR Depacking Procedure
Upscaling in
Horizontal Direction
Splitting & Upscaling in
Vertical by 2
H
W
W
H
= (
H
WRD*6
H
W
H
W
H
W- WRD*2
H
WRD
WRD
H
WRD*2
H
WRD
WRD
View and Depth Splitting
Inverse YCbCr Color Format Conversion
Vertical Flipping & Combination
Get Depth Pixel from
RGB Subpixels Channel
Upscaling in
Horizontal Direction
Depth Enhancement
(Optional)
Splitting & Upscaling in
Vertical by 2
W
W
W- WRD*2
depth_sampling_factor = 1, FaW =(W/24k)*k
depth_sampling_factor = 2, FaW =(W/12k)*k
depth_sampling_factor = 3, FaW =(W/8k)*k

## Slide 16: Centralized Texture-Depth Packing (CTDP) SEI Message Syntax

## Slide 17: CTDP SEI Syntax
centralized_texture-depth_packing( payloadSize ) { | Descriptor
centralized_texture-depth_packing_cancel_flag | u(1)
if( ! centralized_texture-depth_packing_cancel_flag) { | 
depth_sampling_factor | u(3)
packed_depth_size_factor | u(2)
centralized_texture-depth_packing_content_interpretation_type | u(3)
depth_spatial_flipping_flag | u(1)
depth_subpixel_arrangement_type | u(2)
texture_sampling_type | u(3)
depth_sampling_type | u(3)
depth_chroma_sampling_type | u(3)
centralized_texture-depth_packing_persistence_flag | u(1)
} | 
} | 

## Slide 18: depth_sampling_factor
Value | Interpretation
0 | Unspecified the downscale method between the centralized texture-depth packed constituent frames.
1 | Each depth frame in centralized texture-depth packing arrangement represents about 4:1 decimation from the original depth frame horizontally or vertically and about 12:11 decimation from the original texture frame horizontally or vertically, starting from the top or left-most sample.
2 | Each depth frame in centralized texture-depth packing arrangement represents about 4:2 decimation from the original depth frame horizontally or vertically and about 12:10 decimation from the original texture frame horizontally or vertically, starting from the top or left-most sample.
3 | Each depth frame in centralized texture-depth packing arrangement represents about 4:3 decimation from the original depth frame horizontally or vertically and about 12:9 decimation from the original texture frame horizontally or vertically, starting from the top or left-most sample.

## Slide 19: packed_depth_size_factor
packed_depth_size_factor indicates that the heights of reduced depth and texture regions for CTDP-TB format or the width of reduced depth and texture regions for CTDP-LR format are all multiple of 2packed_depth_size_factor+1. It is noted that the value of packed_depth_size_factor is only permitted when the height of image is multiple of 2packed_depth_size_factor+1 for CTDP-TB format and the width of image is multiple of 2packed_depth_size_factor+1 for CTDP-LR format.

## Slide 20: centralized_texture-depth_packing_content_interpretation_type
Value | Interpretation
0 | Indicates that the packed frame is arranged in order of reduced_depth_top (RDT), resized_texture (RT), and reduced_depth_bottom (RDB) from top to bottom called as CTDP TB type as illustrated in Figure D‑X1.
1 | Indicates that the packed frame is arranged in order of reduced_depth_left (RDL), resized_texture (RT), and reduced_depth_right (RDR) from left to right called as CTDP LR type as illustrated in Figure D‑X2.
2 | Indicates that the packed frame, which provides two texture-plus-depth views, is arranged in order of reduced_depth_leftview_top (RDLT), reduced_depth_rightview_top (RDRT), resized_texture_leftview (RTL), resized_texture_rightview (RTR), reduced_depth_leftview_bottom (RDLB), and reduced_depth_rightview_bottom (RDRB),, from upper left, upper right to lower right called as CTDP 2TB type as illustrated in Figure D‑X3.
3 | Indicates that the packed frame, which provides two texture-plus-depth views, is arranged in order of reduced_depth_topview_left (RDTL), reduced_depth_bottomview_left (RDBL), resized_texture_topview (RTT), resized_texture_bottomview (RTB), reduced_depth_topview_right (RDTR) and reduced_depth_bottomview_right (RDBR) from upper left, upper center to lower right called as CTDP 2LR type as illustrated in Figure D‑X4.
CTDP-TB
CTDP-LR
CTDP-2TB
CTDP-2LR

## Slide 21: depth_spatial_flipping_flag
depth_spatial_flipping_flag indicates that the reduced depth region are spatially flipped relative to its intended orientation for display or other such purposes
Value | Interpretation
0 | No flipping
1 | Flipping
HRD
HRD
w
w
HRD
HRD
w
w
No flipping
Flipping

## Slide 22: depth_subpixel_arrangement_type = 0

## Slide 23: depth_subpixel_arrangement_type = 1

## Slide 24: texture_sampling_type
texture_sampling_type indicates that the method of the texture sampling is used by an encoder to indicate to a decoder as specified in Table DX‑3.
Value | Interpretation
1 | Encoder using bilinear method to downscale the vertical or horizontal resolution of texture frame
2 | Encoder using bicubic method to downscale the vertical or horizontal resolution of texture frame

## Slide 25: depth_sampling_type
depth_sampling_type indicates that the method of the depth sampling is used by an encoder to indicate to a decoder as specified in Table DX‑4.
Value | Interpretation
1 | Encoder using bilinear method to downscale the vertical or horizontal resolution of depth frame
2 | Encoder using bicubic method to downscale the vertical or horizontal resolution of depth frame

## Slide 26
depth-chroma_sampling_type indicates that the depth chroma sampling method from 444 to 422 or 420 format is used by an encoder to indicate to a decoder as specified in Table D-X5.
depth_chroma_sampling_type
Value | Interpretation
1 | Encoder using the direct sample to convert the chroma sample from 444 to 422 or 420 format according to marked chroma sample location.
2 | Encoder using the mean of two (four) samples to convert the chroma sample from 444 to 422 (420) format.

## Slide 27: Depth Enhancement for CTDP Format

## Slide 28: CTDP-LR Depacking Procedure
Upscaling in
Horizontal Direction
View and Depth Splitting
Inverse YCbCr Color Format Conversion
Horizontal Flipping & Combination
Get Depth Pixel from
RGB Subpixels Channel
Upscaling in Horizontal Direction (bicubic)
W
W
W-WRD*2
WRD
WRD
W-WRD*2
H
H
H
H
Depth Refinement
YCbCr Calibration

## Slide 29: YCbCr Calibration (for 4:2:0 format)
Y | Cb | Cr | Y | U | V | Y | Cb | Cr | Y | U | V | Y | Cb | Cr | Y | U | V
Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Y | Cb | Cr | Y | U | V | Y | Cb | Cr | Y | U | V | Y | Cb | Cr | Y | U | V
Y | U | V | Y | U | V | Yc | U | V | Y | U | V | Y | U | V | Y | U | V
Y | Cb | Cr | Y | U | V | Y | Cb | Cr | Y | U | V | Y | Cb | Cr | Y | U | V
Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Reference Pixels
1. Find the best-matched Y with the minimum difference value of Yc from reference Y pixels
Cb | Cr
Target pixel
2. Fill Cb and Cr of Yc by using Cb and Cr of the best-matched Y

## Slide 30
Depth Refinement
before
after

## Slide 31: Experimental Results
Environment Settings
Coding performance in HEVC HM 13.0 (CTDP)
Coding performance in 3D-HEVC HTM 8.0

## Slide 32
Sequence | Resolution | Frames | Coded View | Synthesized View
Poznan Hall | 1920*1088 | 200 | 6 | 5
Poznan Street | 1920*1088 | 250 | 4 | 3
Kendo | 1024*768 | 300 | 3 | 4
Balloons | 1024*768 | 300 | 3 | 5
Newspaper | 1024*768 | 300 | 4 | 6
Test Sequences (Nature)

## Slide 33: Experimental Settings
Encoding Mode: All Intra, Low delay, Random access
QP: 27,32,37,42
depth_sampling_factor: 5/6
CTDP_content_interpretation_type: CTDP-LR/TB
image resizing: bicubic
  depth resizing: bicubic
  depth spatial flipping: flipped
  depth subpixel arrangement: sequential order
  depth_chorma_sampling: direct sample

## Slide 34: Experimental Results (1V1D) HEVC + CTDP-TB/LR + DE with respect to 3D-HEVC
BDBR |  |  |  |  |  |  |  |  |  | 
 | Case 1 (without DIBR) % |  |  |  |  |  | Case 2 (DIBR) % |  |  | 
 | Texture |  | Depth |  |  |  | Texture |  |  | 
 | 5/6_TB | 5/6_LR | 5/6_TB | 5/6_TB_DE | 5/6_LR | 5/6_LR_DE | 5/6_TB | 5/6_TB_DE | 5/6_LR | 5/6_LR_DE
ra | 10.7136 | 12.9911 | -42.4982 | -47.0694 | -37.0339 | -41.7659 | 48.8943 | 42.9057 | 73.2979 | 71.1128
ldp | 5.9081 | 9.1367 | -60.5437 | -63.2642 | -55.6811 | -59.4658 | 30.9208 | 25.9498 | 50.1587 | 47.6359
ai | 1.0943 | 1.9308 | -29.7676 | -34.9516 | -23.6991 | -28.9122 | 34.1673 | 29.2253 | 56.7791 | 55.1875
ave | 5.9053 | 8.0196 | -44.2698 | -48.4284 | -38.8047 | -43.3813 | 37.9941 | 32.6936 | 60.0786 | 57.9787
BDPSNR |  |  |  |  |  |  |  |  |  | 
 | Case 1 (without DIBR) dB |  |  |  |  |  | Case 2 (DIBR) dB |  |  | 
 | Texture |  | Depth |  |  |  | Texture |  |  | 
 | 5/6_TB | 5/6_LR | 5/6_TB | 5/6_TB_DE | 5/6_LR | 5/6_LR_DE | 5/6_TB | 5/6_TB_DE | 5/6_LR | 5/6_LR_DE
ra | -0.3945 | -0.4758 | 2.1916 | 2.3961 | 1.6986 | 1.9095 | -1.0967 | -1.0013 | -1.5741 | -1.5513
ldp | -0.2657 | -0.3779 | 3.8679 | 4.0752 | 3.2761 | 3.5311 | -0.7968 | -0.7005 | -1.2681 | -1.2370
ai | -0.0574 | -0.1116 | 1.7845 | 2.0004 | 1.1862 | 1.4016 | -1.0646 | -0.9546 | -1.6084 | -1.5977
ave | -0.2392 | -0.3218 | 2.6147 | 2.8239 | 2.0536 | 2.2807 | -0.9860 | -0.8855 | -1.4835 | -1.4620
DE : depth enhancement

## Slide 35
Original depth
3D HTM , PSNR=39.7431dB
CTDP, PSNR=40.5975dB
CTDP+DE, PSNR=41.0578dB

## Slide 36
Original DIBR synthesis view
3D HTM , PSNR=34.3709dB
CTDP, PSNR=32.8509dB
CTDP+DE, PSNR=33.0167dB

## Slide 37
3D HTM , PSNR=34.3709dB

## Slide 38
CTDP, PSNR=33.0167dB

## Slide 39: Adoption Plans of CTDP Formats

## Slide 40: ChungHwa Telecom’s Adoption Plan
Chunghwa Telecom (CHT) Company with about 1.4 million MOD users has signed an agreement to adopt CTDP format as the following:
1. 09/01/2015: Propose and confirm the test and adoption detailed plan
2. 02/01/2016: Test of downloaded 3D CTDP services with computer clients
(Internal test in CHT and TOUCH Center only)
3. 05/01/2016: Services of 3D MOD services for computer clients
(Charge and open to the public and final CTDP format selection)
4. 11/01/2017: Test of 3D MOD services through Set-top-Boxes with separated CTDP depacking module (Open for selected users)
5. 11/01/2018：Test of 3D MOD services through Set-top-Boxes with Integrated
CTDP depacking module (charged 3D services)

## Slide 41: Hsin Yeong An’s Adoption Plan
Hsin Yeong An (HYA) Cable TV Company with about 145 thousand users is a local cable company near the National Cheng Kung University. The test and adoption plan with time lines are designed as the following:
1. 09/01/2015: Propose and confirm the test and adoption detailed plan
2. 02/01/2016: Test of downloaded 3D CTDP services with computer clients
(Internal test in HYA and TOUCH Center only)
3. 11/01/2016: Services of 3D CATV services for computer clients
(Charge and open to the public and final CTDP format selection)
4. 11/01/2017: Test of 3D CATV services through Set-top-Boxes with separated CTDP depacking module (Open for selected users)
5. 11/01/2018：Test of 3D CATV services through Set-top-Boxes with Integrated CTDP depacking module (charged 3D services)

## Slide 42: First Stage of 3D Service Delivery in Taiwan
2D
TV
Naked-eye
3D TV
CTDP
Depacker
Exiting
STB
DIBR
Engine
New
Glasses
3D TV
RB-glasses
3D Services
2D TV
SBS
Packing
Old
3D TV
3D Effect Control
Multi-view
Two-View
SbS 3D Video
Mixed 2-View to RB 3D
CTDP
3D
Programs
HDMI
HDMI
HDMI
HDMI
HDMI

## Slide 43: Conclusions
This modified CTDP SEI Message is an update of the prior contributions JCT3V-J0108 and JCT3V-K0027. We add a parameter, callled packed_depth_size_factor, to control the size of half reduced depth regions to be multiple of 2, 4, 8, or 16.
With depacking depth enhancement, the objective performances of the proposed texture-5/6 CTDP formats with LR, TB configurations are compared to those by 3D-HEVC.
Once CTDP SEI Message is accepted by MPEG, ChungHwa Telecom MOD System and Hsin-Yeong An Cable TV Company will adopt CTDP formats for their 3D video services in Taiwan.
Not limited to HEVC, the CTDP formats can be applied to all video coders, such as MPEG-2, H.264/AVC. Actually, we are targeting CTDP-H.264/AVC in Taiwan.
If possible, the CTDP formats can be also considered to merge to the existed texture-depth packing format.

## Slide 44
Thanks for your kind attention
Q&A